TEST REPORT

ATC-6120 BIOS

| Version |  | BIOS: V2.0 03 |  |
| --- | --- | --- | --- |
| Testing Period |  | 6th May—22nd May 1998 |  |
| Testing Engineer |  | Allen Hsu Signature: |
| Report Editor |  | Allen Hsu Signature: Steven Chen Signature: |
| Approved by |  | Joe Chen Signature: |

# A-trend Technology Co., Ltd.

# 10F, No. 75, Hsin Tai Wu Rd., Sec. 1, Hsi Chih, Taipei Hsien, Taiwan 221, R.O.C.

# Tel: 886-2-26982199 	 Fax: 886-2-26982369

TABLE OF CONTENTS

SUMMARY	2

PART A BIOS FUNCTION TEST	3

1.Key Components of Test Environment	3

2. Feature Test	3

PART B COMPATIBILITY TEST	6

PART C BURN-IN TEST	7

List of Tables

Table 1. IRQ Function Test in ISA Slot	5

Table 2. IRQ Function Test in PCI Slot	5

Table 3. Compatibility Test for Interconnecting Hardware Components	6

# SUMMARY

## 1.Test Objective

The aim of this report is to record the BIOS test result of LX-440B. The test items include BIOS function test, compatibility test, burn-in test and any possible problems that may have occurred during test.

## 2.Overall Result

| Test Item | Test Procedure | Test Result |
| --- | --- | --- |
| BIOS Function Test | Test each BIOS function both in default and manual setting mode | Bug* |
| Compatibility Test | Compatibility test for interconnecting hardware components (F.D.D./H.D.D./CD-ROM/ZIP/LS-120) | Pass |
| Performance Test | WinNT 4.0 workstation SP3 Runs Winstone98 | Pass |

*: When we test the CMOS SETUP UTILITY, we find a problem under the

INTEGRTED PERIPHERALS in Init AGP Display First which is always Enabled.

- Please see TSD’s bug report sheet No:870511. This bug will be fixed in next version. ( Informed by software engineering department)

## 3. Test Highlights

Test Item

Compatibility Test (H/W)

Modify incompatibility between motherboard and one particular PS/2 mouse

Resolve the error message problem which occurred in the function of DMI (LDCM)

Resolve exclamation mark problem when using PCI sound card

Add the associated information about Intel’s new CPU “Celeron”

Resolve the problem of unable to turn on the computer with STB NITRO DVD AGP card

Add new Micro code 0651

# PART A BIOS FUNCTION TEST

## 1.Key Components of Test Environment

Test Environment

| Motherboard : ATC-6120 V2.1 R12 (L2 Cache 512K) |
| --- |
| CPU | Pentium II 350 (66x5) | VGA Card | ATC-2325B |
| BIOS | Ver 2.0 03 MB (29C010) | LAN Card | D-Link DE220CT |
| RAM | Mitsubishi SDRAM 64MB | K/B | Standard 102 Key |
| H.D.D. | Quantum Fireball 3.2GB 3240AT ST32A013 REV 02-C | Mouse | PS2 |
| F.D.D. | NEC 1.44” FD1231H | Monitor | Philips 17ACM38 |
| CD-ROM | NEC CDR-1800A 5028695303256 | Power Supply | Enhance ATX1025 S/N:E970503224 |

## 2. Feature Test

Main Menu of Award BIOS CMOS Setup Utility

| Item | Result | Item | Result |
| --- | --- | --- | --- |
| 1. STANDARD CMOS SETUP | Pass | 8. INTEGRATED PERIPHERALS | Bug* |
| 2. BIOS FEATURES SETUP | Pass | 9. SUPERVISOR PASSWORD | Pass |
| 3. CHIPSET FEATURES SETUP | Pass | 10. USER PASSWARD | Pass |
| 4. POWER MANAGEMNET SETUP | Pass | 11. IDE HDD AUTO DETECTION | Pass |
| 5. PNP/PCI CONFIGURATION | Pass | 12. HDD LOW LEVEL FORMAT | Pass |
| 6. LOAD BIOS DEFAULT | Pass | 13. SAVE & EXIT SETUP | Pass |
| 7. LOAD SETUP DEFAULT | Pass | 14. EXIT WITHOUT SAVING | Pass |

*: When we test the CMOS Setup Utility, we find a problem under the INTEGRTED PERIPHERALS in Init AGP Display First which is always Enabled.

- Please see TSD’s bug report sheet No:870511. This bug will be fixed in next version. ( Informed by software engineering department)

| ITEM | Test Environment | Test Result |
| --- | --- | --- |
|  | Test Equipment | Test Procedure |  |
| CPU Vcore Measure | Multi-meter |  | Pass |
| CPU Vio Measure | Multi-meter |  | Pass |
| M/B Signon Message | Intel Celeron CPU | Power On | Pass |
| Update BIOS | Awdflash.exe | Awdflash.exe | Pass |
| Load BIOS Default |  | BIOS | Pass |
| Clear CMOS | Shorter | BIOS | Pass |
| ATX Power on | Power on Pins | BIOS | Pass |
|  | PS/2 Mouse |  | Pass |
|  | Password Keys |  | Pass |
|  | Ctrl+F1 Keys |  | Pass |
|  | Resume by Alarm |  | Pass |
|  | Wake on LAN |  | Pass |
| ATX Power off | Power on Pins |  | Pass |
|  |  | Ewin95 Osr2 | Pass |
| CPU Jumper Setting | Shorter / DIP Switch | BIOS | Pass |
| CPU Jumpless Setting | Ins key | BIOS | Pass |
| FDD Bootable | 1.44MB (3.5”) | DOS 6.22 / Format | Pass |
|  | 1.2MB (5.25”) | DOS 6.22 / Format | Pass |
| IDE HDD Bootable | IDE HDD Quantum Bigfoot 4.3GB | DOS 6.22 / Format | Pass |
| Reset | Reset pins | DOS 6.22 | Pass |
|  | Ctrl+Alt+Del keys | DOS 6.22 | Pass |
|  | Ctrl+Alt+Del keys | Ewin95 Osr2 | Pass |
| ISA Slot | ET-4000AX VGA Card | DOS 6.22 | Pass |
| PCI Slot | S3 Trio64 V2 / DX ( VGA Card ) | DOS 6.22 | Pass |
| AGP Slot | ATI 3D Rage Pro ( AGP Card ) | DOS 6.22 | Pass |
| ISA / PCI / AGP Slot Occupied Test | ISA 1 | Debug Card | Ewin95 Osr2 DOS 6.22 | Pass |
|  | ISA 2 | Creative Labs SB16(Sound Card) |  | Pass |
|  | PCI 1 | S3 Trio64 V2 / DX ( VGA Card ) |  | Pass |
|  | PCI 2 | DEC 21040-AA ( LAN Card ) |  | Pass |
|  | PCI 3 | NCR 53C810(SCSI Card) |  | Pass |
|  | AGP | ATI 3D Rage Pro ( AGP Card ) |  | Pass |
| PS/2 | PS/2 Mouse | Ewin95 Osr2 | Pass |
| ISA IRQ Plug & Play | Creative SB16(Sound card) | Ewin95 osr2 | Pass |
|  | D-Link DE220CT/UMC 9003F (LAN card) |  |  |
| ISA IRQ | UMC-9003F, 3-COM-3C509B (LAN card) | Ewin95 Osr2 | Table 1 |
| PCI IRQ | Digital 21040-A(LAN card), 3COM 3C595-7X(LAN Card) S3 Trio 64V2/DX(VGA card) | Ewin95 Osr2 | Table 2 |

#### 【Table 1 IRQ Function Test in ISA Slot】

| IRQ | ISA Slot | ISA Card | Remark | Test Result |
| --- | --- | --- | --- | --- |
| 3 | 1~3 | UMC-9003F | Connect to NT-Server and copy files | Pass |
| 4 | 1~3 | UMC-9003F |  | Pass |
| 5 | 1~3 | UMC-9003F |  | Pass |
| 7 | 1~3 | UMC-9003F |  | Pass |
| 9 | 1~3 | UMC-9003F |  | Pass |
| 10 | 1~3 | UMC-9003F |  | Pass |
| 11 | 1~3 | UMC-9003F |  | Pass |
| 12 | 1~3 | UMC-9003F |  | Pass |
| 14 | 1~3 | D-Link DE-220CT |  | Pass |
| 15 | 1~3 | D-Link DE-220CT |  | Pass |

#### 【Table 2 IRQ Function Test in PCI Slot】

| IRQ | PCI Slot | PCI Card | Remark | Test Result |
| --- | --- | --- | --- | --- |
| 3 | 1~4 | 3-COM-3C595TX | Connect to NT-Server and copy files | Pass |
| 4 | 1~4 | 3-COM-3C595TX |  | Pass |
| 5 | 1~4 | 3-COM-3C595TX |  | Pass |
| 7 | 1~4 | D-Link DE-500CT |  | Pass |
| 9 | 1~4 | D-Link DE-500CT |  | Pass |
| 10 | 1~4 | D-Link DE-500CT |  | Pass |
| 11 | 1~4 | D-Link DE-500CT |  | Pass |
| 12 | 1~4 | 3-COM-3C509B |  | Pass |
| 14 | 1~4 | Digital 21040A |  | Pass |
| 15 | 1~4 | Digital 21040A |  | Pass |

# PART B COMPATIBILITY TEST

Test Environment

| Motherboard : ATC-6120 V2.1 R12 (L2 Cache 512K) |
| --- |
| CPU | Pentium II 350 (66x5) | VGA Card | ATC-2325B |
| BIOS | Ver 2.0 03 MB (29C010) | LAN Card | D-Link DE220CT |
| RAM | Mitsubishi SDRAM 64MB | K/B | Standard 102 Key |
| H.D.D. | Quantum Fireball 3.2GB 3240AT ST32A013 REV 02-C | Mouse | PS2 |
| F.D.D. | NEC 1.44” FD1231H | Monitor | Philips 17ACM38 |
| CD-ROM | NEC CDR-1800A 5028695303256 | Power Supply | Enhance ATX1025 S/N:E970503224 |

| Devices Information |
| --- |
|  | MANAFACTURER | MODEL | SPEC / DRIVER |
| VGA Card | A-Trend | ATC-2325B | 2.00.18 |
| H.D.D | Quantum | Fireball | 3.2GB |
| CD-ROM | NEC | CDR-1800A | 24X |
| LS-120 | MATSUSHITA | LKM-F434-1 | 120MB |
| ZIP | Iomaga | Z100ATAPI | 100MB |

| ITEM | Test Environment | Test Result |
| --- | --- | --- |
|  | Test Equipment | Test Procedure |  |
| F.D.D. | 5.25” 1.2MB 3.5”1.44MB | DOS 6.22 | Pass |
| IDE | H.D.D. CD-ROM | DOS 6.22 CD-ROM Driver | Pass |
|  | H.D.D. CD-ROM LS-120 ZIP | DOS 6.22 CD-ROM Driver LS120 Driver ZIP Driver | Table 3 |
| SCSI | NCR 53C875 | Ewin95 R2 | Pass |
|  | NCR 53C810A |  |  |

#### 【Table 3 Compatibility Test for Interconnecting Hardware Components】

| IDE 1 Master | IDE 1 Slave | IDE 2 Master | IDE 2 Slave | Test Result |
| --- | --- | --- | --- | --- |
| ZIP-100 | LS-120 | H.D.D. | CD-ROM | Pass |
| ZIP-100 | CD-ROM | LS 120 | H.D.D. | Pass |
| ZIP-100 | H.D.D. | CD-ROM | LS-120 | Pass |
| LS 120 | ZIP-100 | CD-ROM | H.D.D. | Pass |
| LS-120 | CD-ROM | ZIP-100 | H.D.D. | Pass |
| H.D.D. | ZIP-100 | LS-120 | CD-ROM | Pass |
| H.D.D. | CD-ROM | ZIP-100 | LS-120 | Pass |
| CD-ROM | ZIP-100 | H.D.D. | LS-120 | Pass |

# PART C BURN-IN TEST

Test Environment

| Motherboard : ATC-6120 V2.1 R12 (L2 Cache 512K) |
| --- |
| CPU | Pentium II 350 (66x5) | VGA Card | ATC-2325B |
| BIOS | Ver 2.0 03 MB (29C010) | LAN Card | D-Link DE220CT |
| RAM | Mitsubishi SDRAM 64MB | K/B | Standard 102 Key |
| H.D.D. | Quantum Fireball 3.2GB 3240AT ST32A013 REV 02-C | Mouse | PS2 |
| F.D.D. | NEC 1.44” FD1231H | Monitor | Philips 17ACM38 |
| CD-ROM | NEC CDR-1800A 5028695303256 | Power Supply | Enhance ATX1025 S/N:E970503224 |

| WinNT 4.0 Workstation SP3 |
| --- |
| ITEM | Time | Test Result |
| Winstone98 Demo | 9:00am May 19, 1998 to 9:00am May 20, 1998 | Pass |