TABLE OF CONTENT

Chapter 1

Features of This Motherboard	1

Chapter 2

Installation	2

2-1   Map of the Motherboard	2

2-2   Installation Steps	4

2-2-1   Jumper Settings	4

2-2-2   System Memory (DRAM)	8

2-2-3   Level 2 External Static RAM (SRAM) Cache	9

2-3   Central Processing Unit (CPU)	9

2-4   Expansion Cards	10

2-5   External Connectors	12

Chapter 3

AWARD BIOS SETUP	19

3-1  STANDARD CMOS SETUP	20

3-2  BIOS FEATURES SETUP	21

3-3  CHIPSET FEATURES SETUP	25

3-4  POWER MANAGEMENT SETUP	26

3-4-1  The Description of the Power Management	27

3-4-2  Description of the Green Functions	28

3-5  PNP/PCI CONFIGURATION SETUP	29

3-6  INTEGRATED PERIPHERALS SETUP	30

3-7  LOAD SETUP DEFAULTS	33

3-8  CHANGE PASSWORD	33

3-9  IDE HDD AUTO DETECTION	34

3-10  SAVE & EXIT SETUP	36

3-11  EXIT WITHOUT SAVING	36

3-12  I/O & MEMORY MAP	37

3-13  TIME & DMA CHANNELS MAP	39

3-14  INTERRUPT MAP	39

3-15  RTC & CMOS RAM MAP	40

3-16  BIOS REFERENCE-POST CODES	41

Chapter 1

Features of This Motherboard

The J-656VXB/J-656VXBP is designed for the PC user who wants a great many features in a small package.  This motherboard:

Easy Installation: Is equipped with BIOS supports auto detection of hard drives and plug and play to make setup of hard drives and expansion cards virtually automatic.

Intel chipset: Intel’s 430VX PCIset with I/O subsystems.

Multi-Speed Support: Support one 75~200Mhz Pentium CPU on a ZIF Socket 7.

L2 Cache: Provides the option of 0KB upgradeable to 256KB or 512KB with Synchronous Cache Module, or on board 256KB upgradeable to 512KB, or on board 512KB Pipelined Burst SRAM.

DRAM Memory Support: Supports 72-pin SIMMs of 4MB, 8MB, 16MB, 32MB, or 64MB to from a memory size between 8MB to 128MB. Support both Fast Page Mode and Extended Data Output (EDO) SIMMs. Support 1 pcs 168-pin 3V unbuffer Synchronous DRAM (DIMM).

ISA and PCI Expansion Slots: Provides four 16-bit ISA slots, three 32-bit PCI slots.

Super Multi-I/O: Provides two high-Speed UART compatible serial ports and one parallel port with EPP and ECP capabilities.  UART2 can also be directed to the Infrared Module for wireless connections. Two floppy drives of either 5.25” or 3.5” (1.44MB or 2.88MB) are also supported without an external card.

PCI Bus Master IDE Controller: On-board PCI Bus Master IDE controller with two connectors that supports four IDE devices in two channels, provides faster data transfer rates, and supports Enhanced IDE devices such as Tape Backup and CD-ROM drives.  This controller supports PIO Modes 3 and 4 and Bus Master IDE DMA Mode 2.

Optional PS/2: This motherboard supports an optional PS/2 mouse cable set.

Chapter 2

Installation

2-1  Map of the Motherboard

Figure 2-1

Jumpers

JP33				p. 4	 Flash ROM voltage Setting (Yellow color selector)

JP22				p. 5	 System Clock Selection (Black color selector)

JP13, JP14		p. 4	 CPU to Bus Frequency Ratio (Blue color selector)

J5				p. 4	 CPU External clock (Bus) Frequency Selection 							 (White color selector)

JP24, JP25, JP26	p. 6	 Voltage Regulator Output Selection (Yellow

J11, J12, J13			 color selector)

JP35				p. 6	 CMOS RAM (Operation/Clear CMOS Data)

(Yellow color selector)

JP7, JP8, JP1, JP2	p. 7	 Level 2 Cache Size setting (Black color selector)

JP29				p. 8	 PS/2 Mouse on IRQ12 setting (Black color

selector)

Connectors

J1				p. 13	 PS/2 Mouse connector (6-pin Block)

JP5				p. 12	 Keyboard connector (5-pin Female)

J2				p. 12 Power connector (12-pin block)

JP9, JP6			p. 13	 Serial Port COMA & COMB (10-pin Block)

PRINT			p. 13	 Parallel Port connector (26-pin Block)

FDC				p. 14	 Floppy Driver connector (34-pin Block)

IDE1				p. 14	 Primary IDE connector (40-pin Block)

IDE2				p. 15	 Secondary IDE connector (40-pin Block)

Keylock			p. 16	 Keyboard Lock Switch (5-pins)

Speaker			p. 16	 Speaker connector (4-pins)

TB.LED			p. 16	 Turbo LED connector (2-pins)

RST				p. 15	 Reset Switch lead (2-pins)

SMI				p. 16	 SMI Switch lead (2-pins)

HD.LED			p. 17	 IDE LED activity light

JP21				p. 17	 CPU 12V Cooling Fan connector

JP23				p. 18  CMOS Battery and Ext Battery connector

Expansion Slots

DIMM			p. 8	 Synchronous DRAM Memory Expansion Slots

SRAM Module		p. 9	 Socket for Pipelined Burst SRAM Cache Module

SIMM Slots		p. 8	 DRAM Memory Expansion slots

ZIF Socket 7		p. 9	 Socket for Central Processing Unit (CPU)

ISA 1,2,3,4		p. 11	 16-bit ISA Bus Expansion slots

PCI 1,2,3			p. 11	 32-bit PCI Bus Expansion slots

2-2  Installation Steps

Before using your computer, you must follow the steps as follows:

Set Jumpers on the Motherboard

Install the CPU

Install DRAM Modules

Install Expansion card

Connect Cables, Wires, and Power Supply

Setup the BIOS Software

2-2-1  Jumper Settings

Flash ROM Voltage Selection:  JP33 (Yellow color selector)

These jumpers set the voltage supplied to the Flash ROM. It depend on Flash ROM Brand.

Selections		JP33

+12V			 1-2		(Intel, MXIC)

+5V			 2-3		(SST, Winbond)

CPU External (Bus) Frequency Selection:  J5 (White color selector)

These jumpers sets the clock generator what frequency to send to the CPU, These allow the selection of the CPU’s External frequency (or Bus Clock).

The Bus Clock times the Bus Ratio equals the CPU’s Internal frequency (the

advertised CPU speed).

CPU to Bus Frequency Ratio:  JP13, JP14 (Blue color selector)

These jumpers set the frequency ratio between the Internal frequency of the CPU and the External frequency (Bus Clock) within the CPU.  These must be set together with the bellow jumpers CPU External (Bus) frequency Selection (J5).

J-656VXB/J-656VXBP Jumper Setting for CPU

| CPU Type | Ratio | External | J5 | JP13 | JP14 |  |
| --- | --- | --- | --- | --- | --- | --- |

P55C-200MHz

P54C-200MHz

3.0x

66MHz

open

open

| short |  |
| --- | --- |

P55C-166MHz

P54C-166MHz

2.5x

66MHz

open

short

| short |  | P54C-150MHz | 2.5x | 60MHz | 5-6 | short | short |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

P54C-133MHz

Cyrix 6X86-166+

IBM 6X86-166+

2.0x

66MHz

open

short

| open |  |
| --- | --- |

P54C-120MHz

Cyrix 6X86-150+

IBM 6X86-150+

2.0x

60MHz

5-6

short

| open |  |
| --- | --- |

P54C-100MHz

AMD K5-PR100

AMD K5-PR133

1.5x

66MHz

open

open

| open |  |
| --- | --- |

P54C-90MHz

AMD K5-PR90

1.5x

60MHz

5-6

open

| open |  | Cyrix 6X86-133+ | 2.0x | 55MHz | 3-4 | short | open |  | Cyrix 6X86-120+ | 2.0x | 50MHz | 3-4,5-6 | short | open |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

System Clock Setting:  JP22 (Black color selector)

This jumper set the system clock to PCICLK/4 or PCICLK/3

Normal in 60Mhz/66MHz Bus frequency choice PCICLK/4

Normal in 50Mhz Bus frequency choice PCICLK/3

Selections		JP22

PCICLK/4		short

PCICLK/3		open

J-656VXBP Voltage Regulator Output Selection 2 (use Q1, Q2 Regulators)

These jumpers set the Voltage supplied to the CPU.

CPU Core Voltage Output Selection: JP24,JP25,JP26 (Yellow color selector)

Selections		JP24		JP25		JP26

2.8V			short		open		open

3.45V			open		short		open

3.52V 			open		open		short

CPU I/O Voltage Output Selection:  J11, J12, J13 (Yellow color selector)

Selections		J11		J12		J13

3.3V			short		open		open

3.45V			open		short		open

3.52V 			open		open		short

| CPU TYPE | JP24 | JP25 | JP26 | J11 | J12 | J13 |  | Intel P55C | short | open | open | open | short | open |  | Intel P54C | open | short | open | open | short | open |  | AMD K5 ABQ (3.52V) | open | open | short | open | open | short |  | Cyrix 6x86 (3.52V) | open | open | short | open | open | short |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

J-656VXB Voltage Regulator Output Selection 1 (Only use Q1 Regulator) : JP24, JP25, JP26 (Yellow color selector)

Selections		JP24		JP25		JP26

3.3V			short		open		open

3.45V			open		short		open

3.52V 			open		open		short

CMOS RAM: JP35 (Yellow color selector)

This clears the user-entered information stored in the CMOS RAM chip such as hard disk information and passwords.  Simply connect a jumper cap over this jumper for a few seconds then remove. But make sure that your computer is turned off.  You must enter the BIOS setup (by holding down <DEL> during power-up) after this is done to re-enter BIOS information (see BIOS SETUP)

Selections		JP35

Normal		open  (Default)

Clear CMOS	short  (momentarily)

Level 2 Cache Size Setting:  JP7, JP8, JP1, JP2 (Black color selector)

This jumper sets the total amount of L2 cache that is present.  If you have two cache chips on-board, then you have either 256KB or 512KB.  A “COAST” cache module can be used to upgrade the 256KB version to 512KB version.  If there is no on-board cache, you must install a cache module of either 256KB or 512KB.  Regardless of your cache combination, set the following jumpers according to the total amount of L2 cache that is present on-board and install as a module.

Selections		JP7	   JP8      JP1	 JP2

256KB			1-2	   1-2	      1-2	 1-2

256KB+		2-3	   1-2	      2-3	 1-2	   For JET-WAY SRAM Module

Module 256KB

256KB+		1-2	   2-3	      1-2	 2-3	   For Intel SPEC SRAM Module

Module 256KB

PS/2 Mouse on IRQ12 Setting:   JP29 (Black color selector)

JP29 enables or disables the on-board PS/2 mouse lead connector.  When Enabled, the port becomes active and uses IRQ12. See Page 21 for the “PS/2 Mouse connector”.

2-2-2   System Memory (DRAM)

This motherboard supports four 72-pin SIMMs of 4MB, 8MB, 16MB, 32MB, or 64MB to form a memory size between 8MB to 128MB.  The DRAM can be either 60ns or 70ns Fast Page Mode or EDO RAM.  This motherboard also supports one 168-pin DIMM module, it can use only +3V unbuffer Synchronous DRAM.

Install two memory modules each time as shown in the chart below.

Bank 0

SIMM 3 & 4

Bank 1

SIMM 1& 2

Total Memory

| Combination |  | 4MB x 2 | None | 8MB |  | 8MB x 2 | None | 16MB |  | 16MB x 2 | None | 32MB |  | 32MB x 2 | None | 64MB |  | 4MB x 2 | 4MB x 2 | 16MB |  | 4MB x 2 | 8MB x 2 | 24MB |  | 4MB x 2 | 16MB x 2 | 40MB |  | 4MB x 2 | 32MB x 2 | 72MB |  | 8MB x 2 | 4MB x 2 | 24MB |  | 8MB x 2 | 8MB x 2 | 32MB |  | 8MB x 2 | 16MB x 2 | 48MB |  | 8MB x 2 | 32MB x 2 | 80MB |  | 16MB x 2 | 4MB x 2 | 40MB |  | 16MB x 2 | 8MB x 2 | 48MB |  | 16MB x 2 | 16MB x 2 | 64MB |  | 16MB x 2 | 32MB x 2 | 96MB |  | 32MB x 2 | 4MB x 2 | 72MB |  | 32MB x 2 | 8MB x 2 | 80MB |  | 32MB x 2 | 16MB x 2 | 96MB |  | 32MB x 2 | 32MB x 2 | 128MB |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

(	This motherboard supports 3V unbuffered DIMM Modules with SDRAM,  supports 1M x 64, 2M x 64 and 4M x 64 DIMMs

DIMM module always occupy BANK0, please don’t install both DIMM and SIMM module in BANK0.

Example: When you use DIMM module, you can’t plug SIMM module in SIMM3 & SIMM4, just ca plug in SIMM1 & SIMM2.

2-2-3   Level 2 External Static RAM (SRAM) Cache

The motherboard you may purchase may have either 0KB, 256KB or 512KB on board.  If you have two cache chips on-board then you have either 256KB or 512KB pipeline burst SRAM cache, “COAST” cache module can be used to upgrade the 256KB version to 512KB.

256KB PB SRAM Module

2-3  Central Processing Unit (CPU)

The motherboard provides a 321-pin ZIF Socket 7.  The CPU that came with the motherboard sould have a fan attached to it to prevent overheating.  If this is not the cae then purchase a fan before you turn on your system.

WARNING:	Without a fan, the CPU can overheat and cause damage to both the CPU and the motherboard.

To install a CPU, first turn off your system and remove its cover.  Locate the ZIF socket and open it by first pulling the lever sideways away from the socket then upwards to a 90-degree right angle.  Insert the CPU with the white dot as your guide.  The white dot should point towards the end of the level.  The CPU has a corner pin for three of the four corners, the CPU will only fit in the one orientation as shown.  With the added weight of the CPU fan, no force is required to insert the CPU.  Once completely inserted, hold down on the fan and close the socket’s lever.

IMPORTANT: 	You must set jumpers JP13 & JP14 “CPU to Bus frequency Ratio” on and jumpers J5 “Bus Frequency Selection” on page 4 depending on the CPU that you install.

2-4   Expansion Cards

First read your expansion card documentation on any hardware and software settings that may be required to setup your specific card.

Installation Procedure:

Read the documentation for your expansion card.

Set any necessary jumpers on your expansion card.

Remove your computer’s cover.

Remove the bracket on the slot you intend to use.

Carefully align the card’s connectors and press firmly.

Secure the card on the slot with the screw you remove in step 4.

Replace the computer’s cover.

Setup the BIOS if necessary.

Install the necessary software drivers for your expansion card.

Assigning IRQs for Expansion Cards

Some expansion cards need to use an IRQ to operate.  Generally an IRQ  must be exclusively assigned to one use.  In an standard design three are 16 IRQs available but most of them are already in use by parts of the system which leaves 6 free for expansion cards.

Both ISA and PCI expansion cards may need to use IRQs. System IRQs are available to cards installed in the ISA expansion but first, and any remaining IRQs are then used by PCI cards.  Currently, there are two types of ISA cards.  The original ISA expansion card design, now referred to as “Legacy” ISA cards, requires that you configure the card‘s jumpers manually and then install it in any available slot on the ISA bus. You may use Microsoft’s Diagnostic (MSD.EXE) utility included in the Windows directory to see a map of your used and free IRQs.  For Windows 95 users, the “Control Panel” icon in “My Computer”, contains a “System” icon which gives you “Device Manager” tab.  Double clicking on a specific device give you “Resources” tab which shows the Interrupt number and address.  Make sure that no two devices use the same IRQs or your computer will experience problems when those two devices are in use at the same time.

To simplify this process this motherboard has complied with the Plug and Play (PNP) specification which was developed to allow automatic system configuration whenever a PNP-compliant card is added to the system.  For PNP cards, IRQs are assigned automatically from those available.

If the system has both Legacy and PNP ISA cards installed, IRQs are assigned to PNP cards from those not used by Legacy cards.  The PCI and PNP configuration of the BIOS setup utility can be used to indicate which IRQs are being used by Legacy cards.  For older Legacy cards that does not work with the BIOS, you can contact your vendor for an ISA Configuration Utility.

An IRQ number is automatically assigned to PCI expansion cards after those used by Legacy and PNP ISA cards.  In the PCI bus design, the BIOS automatically assigns an IRQ to a PCI slot that has a card in it that requires an IRQ. To install a PCI card, you need to set something called the INT (interrupt) assignment.  Since all the PCI slots on this motherboard use an INTA #, be sure that the jumpers on your PCI cards are set to INT A.

Assigning DMA Channels for ISA Cards

Some ISA cards, both Legacy and PNP may also need to use a DMA (Direct Memory Access) channel.  DMA assignments for this motherboard are handled the same way as the IRQ assignment process described above.  You can select a DMA channel in the PCI and PNP configuration section of the BIOS Setup utility.  In the BIOS setup, you should choose “Yes” for those IRQ‘s and DMA’s you wish to reserve for Legacy cards.

2-5   External Connectors

Power connector (12-pin block): J2

This connector connects to a standard 5 Volt power supply.  To connect the leads from the power supply, ensure first that the power supply is not plugged.  Most power supplies provide two plugs (P8 and P9), each containing six wires, two of which are black.  Orient the connectors so that the black wires are located in the middle.

Using a slight angle, align the plastic guide pins on the lead to their receptacles on the connector. Once aligned, press the lead onto the connector until the lead locks into place.

Keyboard Connector (5-pin female): JP5

This connection is for a standard IBM-compatible keyboard.  May also be known as a 101 enhanced keyboard.

PS/2 Mouse Connector (6-pin block): J1

If you are using a PS/2 mouse, you must purchase an optional PS/2 mouse set which connects to the 6 pin block and mounts to an open slot on your computer‘s case.  You must also set “PS/2 Mouse Selection” on page 21 to enable the PS/2 Mouse.

Parallel Printer Connector (26-pin Block):  PRINT

Connection for the included parallel port ribbon cable with mounting bracket. Connect the ribbon cable to this connection and mount the bracket to the case on an open slot.  It will then be available for a parallel printer cable.

Note:  Serial printers must be connected to the serial port. You can enable the parallel port and choose the IRQ through BIOS Setup on page 32 “Onboard Parallel Port”.

Serial port COMA and COMB Connector (Two 10-pin blocks): JP9, JP6

These connectors support the provided serial port ribbon cables with mounting bracket.  Connect the ribbon cables to these connectors and mount the bracket to the case on an open slot.  The two serial ports on the mounting bracket will then be used for pointing devices or other serial devices.  See page 32 for BIOS configuration of “Onboard Serial Port”

Floppy drive Connector (34-pin block): FDC

This connector supports the provided floppy drive ribbon cable.  After connecting the single end to the board, connect the two plugs on the other end to the floppy drives.

Primary IDE Connector (40-pin block): IDE1

This connector supports the provided IDE hard disk ribbon cable.  After connecting the single end to the board, connect the two plugs at the other end to your hard disk(s).  If you install two hard disks, you must configure the second drive to Slave mode by setting its jumpers accordingly.  Please refer to the documentation of your hard disk for the jumper settings.  See the figure below.

Secondary IDE Connector (40-pin block): IDE2

This connector connects to the next set of Master and Slave hard disks.  Follow the same procedure described for the primary IDE connector. You may also configure two hard disks to be both Masters using one ribbon cable on the primary IDE connector and another ribbon cable on the secondary IDE connector.

Turbo LED switch (TB.LED)

The motherboard‘s turbo function is always on. The turbo LED connection is labeled here but the LED will remain constantly lit while the system power is on.  You may wish to connect the Power LED from the system case to this lead.  See the figure on page 16.

Reset switch lead (RST)

This 2-pin connector connects to the case-mounted reset switch for rebooting your computer without having to turn off your power switch. This is a preferred method of rebooting in order to prolong the life of the system‘s power supply.  See the figure below.

Keyboard lock switch lead (KEYLOCK)

This 5-pin connector connects to the case-mounted key switch for locking the keyboard for security purposes.  See the figure below.

Speaker connector (SPEAKER)

This 4-pin connector connects to the case-mounted speaker.

SMI suspend switch lead (SMI)

This allows the user to manually place the system into a suspend mode or “Green” mode where system activity will be instantly decreased to save electricity and expand the life of certain components when the system is not in use. This 2-pin connector (see the figure below) connects to the case-mounted suspend switch.  If you do not have a switch for the connector, you may use the “Turbo Switch” since it does not have a function. SMI is activated when it detects a short to open moment and therefore leaving it shorted will not cause any problems. May require one or two pushes depending on the position of the switch. Wake-up can be controlled by settings in the BIOS but the keyboard will always allow wake-up (the SMI lead cannot wake-up the system). If you want to use this connector, “Suspend Switch” in the POWER MANAGEMENT SETUP of the BIOS software should be on the default setting of Enable (see page 26).

Selections			SMI

Enter suspend mode	short

Normal			open

IDE activity LED (HD. LED)

This connector connects to the hard disk activity indicator light on the case.

CPU cooling fan connector (JP21)

This connector supports a CPU cooling fan of 500mAMP (6WATT) or less.  Depending on the fan manufacturer, the wiring may be different.  The red wire should be positive, while the black should be ground.  Connect the fan to the board taking into consideration the polarity of the connector.

WARNING:  Damage may occur to the motherboard and/or the CPU fan if these pins are incorrectly used.

CMOS Battery and Ext Battery connector (JP23)

Chapter 3

AWARD BIOS SETUP

Award's ROM BIOS provides a built-in Setup program which allows user modify the basic system configuration and hardware parameters.  The modified data will be stored in a battery-backed CMOS RAM so data will be retained even when the power is turned off.  In general, the information saved in the CMOS RAM stay unchanged unless here is configuration change in the system, such as hard drive replacement or new equipment is installed.

It is possible that CMOS had a battery failure which cause data lose in CMOS_RAM. If so, re_enter system configuration parameters become necessary.

To enter Setup Program

Power on the computer and press <Del> key immediately will bring you into BIOS CMOS SETUP UTILITY.

ROM PCI/ISA BIOS (2A59GJ19)

CMOS SETUP UTILITY

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

STANDARD CMOS SETUP

BIOS FEATURES SETUP

CHIPSET FEATURES SETUP

POWER MANAGEMENT SETUP

PNP/PCI CONFIGURATION

LOAD BIOS DEFAULTS

LOAD SETUP DEFAULTS

INTEGRATED PERIPHERALS

SUPERVISOR PASSWORD

USER PASSWORD

IDE HDD AUTO DETECTION

HDD LOW LEVEL FORMAT

SAVE & EXIT SETUP

| EXIT WITHOUT SAVING |  |
| --- | --- |

Esc : QUIT                       ô¡õ¡÷¡ö¡   : Select Item

| F10 : Save & Exit Setup (Shift) F2 : Change Color |  |  | Time, Date, Hard Disk Type... |  |  |
| --- | --- | --- | --- | --- | --- |

Figure 3-1

The menu displays all the major selection items and allow user to select any one of shown item.  The selection is made by moving cursor (press any direction key) to the item and press <Enter> key.  An on_line help message is displayed at the bottom of the screen as cursor is moving to various items which provides user better understanding of each function.  When a selection is made, the menu of selected item will appear so the user can modify associated configuration parameters.

3-1  STANDARD CMOS SETUP

Choose "STANDARD CMOS SETUP" in the CMOS SETUP UTILITY Menu (Figure 3-1).  The STANDARD CMOS SETUP allows user to configure system setting such as current date and time, type of hard disk drive installed in the system, floppy drive type, and the type of display monitor.  Memory size is auto_detected by the BIOS and displayed for your reference.  When a field is highlighted (direction keys to move cursor and <Enter> key to select), the entries in the field will be changed by pressing <PgDn> or <PgUp> keys or user can enter new data directly from the keyboard.

ROM PCI/ISA BIOS (2A59GJ19)

STANDARD CMOS SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Date (mm:dd:yy) : Fri, Jul, 12  1996

Time (hh:mm:ss) : 18 : 45 : 18

HARD DISKS         TYPE  SIZE  CYLS  HEAD  PRECOMP  LANDZ  SECTOR  MODE

Primary Master   : Auto     0     0     0        0      0       0  Auto

Primary Slave    : Auto     0     0     0        0      0       0  Auto

Secondary Master : Auto     0     0     0        0      0       0  Auto

Secondary Slave  : Auto     0     0     0        0      0       0  Auto

Drive A : 1.2M , 5.25 in.

Drive B : None

Video   : EGA/VGA

Halt On : All Errors

Base  Memory :   640K

Extended  Memory :  7168K

Other  Memory :   384K

| Total Memory : 8192K |  |
| --- | --- |

Esc : Quit             ô¡õ¡÷¡ö¡ : Select Item        Pu/Pd/+/- : Modify

| F1 : Help (Shift)F2: Change Color |  |  |
| --- | --- | --- |

Figure 3-2

NOTE:	If hard disk Primary Master/Slave and Secondary Master/Slave were   used Auto, than the hard disk size and model will be auto-detect on display during POST.

NOTE:	The "Halt On:" field is to determine when to halt the system by the BIOS is error occurred during POST.

3-2   BIOS FEATURES SETUP

Select the "BIOS FEATURES SETUP" option in the CMOS SETUP UTILITY menu allows user to change system related parameters in the displayed menu.  This menu shows all of the manufacturer's default values of J-656VXB/J-656VXBP.  Again, user can move the cursor by pressing direction keys and <PgDn> of <PgUp> keys to modify the parameters.  Pressing [F1] key to display help message of the selected item.

This setup program also provide 2 convinent ways to load the default parameter data from BIOS [F6] or CMOS [F7] area if shown data is corrupted.  This provides the system a capability to recover from any possible error.

ROM PCI/ISA BIOS (2A59GJ19)

BIOS FEATURES SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Virus Warning              : Disabled

CPU Internal Cache         : Enabled

External Cache             : Enabled

Quick Power On Self Test   : Disabled

Boot Sequence              : A,C

Swap Floppy Drive          : Disabled

Boot Up Floppy Seek        : Enabled

Boot Up Numlock Status     : On

Boot Up System Speed       : High

Gate A20 Option            : Fast

Memory Parity Check        : Disabled

Typematic Rate Setting     : Disabled

Typematic Rate (Chars/Sec) : 6

Typematic Delay (Msec)     : 250

Security Option : Setup

Video  BIOS Shadow      : Enabled

C8000-CBFFF Shadow      : Disabled

CC000-CFFFF Shadow      : Dsiabled

D0000-D3FFF Shadow      : Disabled

D4000-D7FFF Shadow      : Disabled

D8000-DBFFF Shadow      : Disabled

DC000-DFFFF Shadow      : Dsiabled

PS/2 mouse function control: Disabled

PCI/VGA Palette Snoop      : Disabled

OS Select For DRAM > 64MB  : Non-OS2

Esc: Quit    ô¡õ¡÷¡ö¡  : Select Item

F1 : Help           Pu/Pd/+/-:Modify

F5 : Old Values    (Shift)F2 : Color

F6 : Load BIOS Defaults

| F7 : Load Setup Defaults |  |
| --- | --- |

Figure 3-3

Note:	The Security Option contians "setup" and "system". The "setup" indicates that the password setting is for CMOS only while the "system" indicates the password setting is for both CMOS and system boot up procedure.

Virus Warning:  This category flashes on the screen.  During and after the system boots up, any attempt to write to the boot sector or partition table of the hard disk drive will halt the system and the following error message will appear, in the mean time, you can run an anti-virus program to locate the problem.  Default value is Disabled

Enabled:	Activates automatically when the system boots up causing a        warning message to appear when anything attempts to access the boot sector or hard disk partition table.

Disabled:	No warning message to appear when anything attempts to access the boot sector or hard disk partition table.

CPU Internal Cache / External Cache:  These two categories speed up memory access.  However, it depends on CPU/chipset design.  The default value is Enable.  If your CPU without Internal Cache then this item "CPU Internal Cache" will not be show.

Enabled:	Enable cachehis category speeds up Power On Self Test. 				(POST) after you power on the comp

Disabled:	Disable cache

Quick Power On Self Test:  Tuter.  If it is set to Enable, BIOS will shorten or skip some check items during POST.

Enabled:	Enable quick POST

Disabled:	Normal POST

Boot Sequence:   This category determines which drive computer searches first for the DOS (Disk Operating System).  Default value is A,C.

A,C:	System will first search for floppy disk drive then hard disk drive.

C,A:	System will first search for hard disk drive then floppy disk drive.

Swap Floppy Drive:  The swap floppy drive.  Default value is Disabled.

Enabled:	Floppy A & B will be swapped under the DOS

Disabled:	Floppy A & B will be not swap

Boot Up Floppy Seek:  During POST, BIOS will determine if the floppy disk drive installed is 40 or 80 tracks.  360K type is 40 tracks while 760K, 1.2M and 1.44M are all 80 tracks.  The default value is Enabled.

Enabled:	BIOS searches for floppy disk drive to determine if it is 40 or 80 tracks.

Note that BIOS can not tell from 720K, 1.2M or 1.44M drive type as they are all 80 tracks.

Disabled:	BIOS will not search for the type of floppy disk drive by track number.

Note that there will not be any warning message if the drive installed is 360K.

Boot Up NumLock Status:  The default value is On.

On:	Keypad is number keys.

Off:	Keypad is arrow keys.

Boot UP System Speed:  It selects the default system speed-the speed that the system will run at immediately after power up.

High:	  Set the speed to high.

Low:	  Set the speed to low.

NOTE: The board default value is LOW in the field. Boot the system to   controller turbo or De-turbo by Onboard (Turbo Switch).

Gate A20 Option:  The default value is Fast.

Normal:	The A20 signal

# Text boxes

BIOS will use default value of this 2 items and the default is controlled by keyboard.

Typematic Rate (Chars/Sec):

6  :   6  cha