TABLE OF CONTENT

Chapter 1

Features of This Motherboard	1

Chapter 2

Installation	2

2-1   Map of the Motherboard	2

2-2   Installation Steps	4

2-2-1   Jumper Settings	4

2-2-2   System Memory (DRAM)	8

2-3   Central Processing Unit (CPU)	9

2-4   Expansion Cards	10

2-5   External Connectors	11

Chapter 3

AWARD BIOS SETUP	16

3-1  STANDARD CMOS SETUP	17

3-2  BIOS FEATURES SETUP	18

3-3  CHIPSET FEATURES SETUP	22

3-4  POWER MANAGEMENT SETUP	23

3-4-1  The Description of the Power Management	24

3-4-2  Description of the Green Functions	25

3-5  PNP/PCI CONFIGURATION SETUP	26

3-6  LOAD BIOS DEFAULTS	27

3-7  LOAD SETUP DEFAULTS	27

3-8  INTEGRATED PERIPHERALS SETUP	28

3-9  SUPERVISOR/USER PASSWORD	31

3-10  IDE HDD AUTO DETECTION	32

3-11  SAVE & EXIT SETUP	34

3-12  EXIT WITHOUT SAVING	34

3-13  I/O & MEMORY MAP	34

3-14  TIME & DMA CHANNELS MAP	36

3-15  INTERRUPT MAP	36

3-16  RTC & CMOS RAM MAP	37

3-17  BIOS REFERENCE-POST CODES	38

Chapter 1

Features of This Motherboard

The design J-656VXD/J-656VXDP is powerful enough for the PC user who needs a great features within a small package.  This motherboard including:

Easy Installation: Is equipped with BIOS supports auto detection of hard drives and plug and play to make setup of hard drives and expansion cards virtually automatic.

Intel chipset: Intel’s 430VX PCIset with I/O subsystems.

Multi-Speed Support: Support one 75~200Mhz Pentium CPU on a ZIF Socket 7.

L2 Cache: 256KB or 512KB with Pipelined Burst SRAM on board.

DRAM Memory Support: Supports 72-pins SIMMs of 4MB, 8MB, 16MB, 32MB, or 64MB to memory size between 8MB to 512MB. Support both Fast Page Mode and Extended Data Output (EDO) SIMMs, and also support 2 pcs 168-pin 3V unbuffer Synchronous DRAM (DIMM).

ISA and PCI Expansion Slots: Provides four 16-bit ISA slots, three 32-bit PCI slots.

Super Multi-I/O: Provides two high-Speed UART compatible serial ports and one parallel port with EPP and ECP capabilities. UART2 can also be directed to the Infrared Module for wireless connections.  Two floppy drives of either 5.25” or 3.5” (1.44MB or 2.88MB) are also supported without an external card.

PCI Bus Master IDE Controller: On-board PCI Bus Master IDE controller with two connectors that supports four IDE devices in two channels, provides faster data transfer rates, and supports Enhanced IDE devices such as Tape Backup and CD-ROM drives. This controller supports PIO Modes 3 and 4 and Bus Master IDE DMA Mode 2.

PS/2 Mouse Connector: This motherboard supports an optional PS/2 mouse cable set.

Optional USB Port Connector: This motherboard supports two USB port connectors for USB devices.

Chapter 2

Installation

2-1  Map of the Motherboard

Figure 2-1

Jumpers

JP4	p. 4	Flash ROM voltage Selection (Yellow color selector)

FS0, FS1, FS2	p. 4	CPU External (Bus) Frequency Selection  (White color			selector)

| BF0, B |
| --- |
|  | Cyr 6xMX-P | 2.5x | 60MHz | open | sh | P54C-133MHz | 2.0x | 66MHz | s | P54C-120MHz | 2.0x | 60MHz | open | short | short | 2-3 | 1-2 |  | P54C-100MHz | 1.5x | 66MHz | short | open | short | 1-2 | 1-2 |  | P54C-90 |
|  | CyrixMX-P | 2.0x | 75MHz | open | sh | Cyrix 6X86-166+ | 2.0x | 66MHz | Cyrix 6X86-150+ | 2.0x | 60MHz | open | short | short | 2-3 | 1-2 |  | Cyrix 6X86-133+ | 2.0x | 55MHz | short | short | open | 2-3 | 1-2 |  | Cyrix 6X86-120+ | 2.0x | 50MHz | short | short | short | 2-3 | 1-2 |  | AMD K5-PR166 | 2.5X | AMD K5-PR90 | 1.5x | 60MHz |

opNOTE:		Before install the CPU, Please check the CPU F

(		For Cyrix 6X86MX series, please double ch

(	7MHCP’s Bus Frequency is not ition, therwe are commd to us

J-656 CPU Voltage Selection (use Q2,(Yellow coor

These jumpers set the Vol

CPU Core Voltage (Q2): JP11

Selections		JP11

2.8V			1-2

3.3V			2-3

3.45V 		4-5

3.52V			5-6

CPU I/O Voltage (Q3

| CPU TYPE | JP11 | JP12 |  | P55C | 1-2 | 1-2 |  | P54C | 4-5 | 1-2 |  | AMD ABQ (3.52V) | 5-6 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Cyrix 6X86

IBM 6X86 (3.52V)

5-6

| 2-3 |  |
| --- | --- |

CMOS RAM: JP5 (Yellow color selector)

This clears the user-entered information stored in the CMOS RAM chip such as hard disk information and passwords.  Simply connect a jumper cap over this jumper for a few seconds then2-2-2   System Memory (DRAM)

This motherboard supports four 72-pin SIMMs of 4MB, 8MB, 16MB, 32MB, or 64MB to from a memorort two 168-pin DIMM Module, it can use only +3V unbuffer synchronous DRAM.

Install two memory modules each time as shown in the chart below.

| Bank 0 | Bank 1 | Total Memory |  | SIMM1 | SIMM2 | SIMM3 | SIMM4 | Combination |  | 4MB | 4MB | none | none | 8MB |  | 4MB | 4MB | 4MB | 4MB | 16MB |  | 8MB | 8MB | none | none | 16MB |  | 8MB | 8MB | 4MB | 4MB | 24MB |  | 8MB | 8MB | 8MB | 8MB | 32MB |  | 16MB | 16MB | none | none | 32MB |  | 16MB | 16MB | 4MB | 4MB | 40MB |  | 16MB | 16MB | 8MB | 8MB | 48MB |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

16MB1: BANK0, DIMM2: BANK1

* 	We don’t recommand use FAST PAGE/EDO Module with DIMM combination.

2-3  Central Processing Unit (CPU)

The motherboard provides a 321-pins ZIF Socket 7. The CPU on mother board must have a fan attached to prevent overheating.

WARNING:	Without a fan, the CPU will overheat and cause damage to both the CPU and the motherboard.

To install a CPU, first turn off your system and remove its cover.  Locate the ZIF socket and open it by first pulling the lever sideways away from the socket then upwards to a 90-degree right angle.  Insert the CPU with the white d

2-4   Expansion Cards

You must read the documentation come with expansion card for any hardware or software settings that may be required to setup your specific card.

Installation Procedure:

Read the documentation from your expansion card.

Set any necessary jumpers on your expansion card.

Remove your computer’s cover.

Remove the bracket on the slot you intend to use.

Carefully align the card’s connectors and press firmly.

Secure the card on the slot with the screw you remove in step 4.

Replace the computer’s cover.

Setup the BIOS if necessary.

Install the necessary software drivers for your expansion card.

Assigning IRQs for Expansion Cards

Some expansion cards may require an IRQ to operate.  Generally an IRQ  must be exclusively assigned to only one device.  In an standard design there are 16 IRQs available but most of them are occupied by the system and leaves 6 free for expansion cards.

Either ISA or PCI expansion cards may require an IRQs. System IRQs are available to cards installed in the ISA expansion first, and any remaining IRQs can be used by PCI cards. Currently, there are two types of ISA cards. An original ISA expansion card design, know as “Legacy” ISA cards, they request configure the card’s jumpers manually and then install it in any available slot on the ISA bus, and other know as Plug and Play. You may use Microsoft’s Diagnostic (MSD.EXE) utility included in the DOS directory to see a map of your used and any free IRQs.  For Windows 95 users, the “Control Panel” icon in “My Computer”, contains a “System” icon which gives you “Device Manager” tab.  Double clicking on a specific device give you “Resources” tab which shows the Interrupt number and address.  Make sure that no any two of devices use the same IRQs, or your computer will experience problems when those two devices are in use at the same time.

To simplify this process the motherboard has complied with the Plug and Play (PNP) specification which was developed to allow automatic system configuration whenever a PNP-compliant card is added to the system.  For PNP cards, IRQs are assigned automatically from those available.

If the system has both Legacy and PNP ISA cards installed, IRQs are assigned to PNP cards from those not used by Legacy cards. The PCI and PNP configuration of the BIOS setup utility can be used to indicate which IRQs are being used by Legacy cards.  For older Legacy cards that does not work with the BIOS, you can contact your vendor for an ISA Configuration Utility.

An IRQ number is automatically assigned to PCI expansion cards after those used by Legacy and PNP ISA cards.  In the PCI bus design, the BIOS automatically assigns an IRQ to a PCI. To install a PCI card, you need to set something called the INT (interrupt) assignment.  Since all the PCI slots on this motherboard use an INTA #, be sure that the jumpers on your PCI cards are set to INT A.

Assigning DMA Channels for ISA Cards

Some ISA cards, both Legacy and PNP may also need to use a DMA (Direct Memory Access) channel.  DMA assignments for this motherboard are handled the same way as the IRQ assignment process described above.  You can select a DMA channel in the PCI and PNP configuration section of the BIOS Setup utility.  In the BIOS setup, you should choose “Yes” for those IRQ’s and DMA’s you wish to reserve for Legacy cards.

2-5   External Connectors

Power connector (12-pin block): JP23

This connector connects to a standard 5 Volt power supply.  To connect the leads from the power supply, ensure first that the power supply is not plugged.  Most power supplies provide two plugs (P8 and P9), each containing six wires, two of which are black.  Orient the connectors so that the black wires are located in the middle.

Using a slight angle, align the plastic guide pins on the lead to their receptacles on the connector. Once aligned, press the lead onto the connector until the lead locks into place.

Keyboard Connector (5-pin female): KB1

This connection is for a standard IBM-compatible keyboard. May also be known as a 101 enhanced keyboard.

PS/2 Mouse Connector (6-pin block): J1

If you are using a PS/2 mouse, you must purchase an optional PS/2 mouse set which connects to the 6 pin block and mounts to an open slot on your computer‘s case.

Parallel Printer Connector (26-pin Block):  PRINT (J7)

Connection for the included parallel port ribbon cable with mounting bracket. Connect the ribbon cable to this connection and mount the bracket to the case on an open slot.  It will then be available for a parallel printer cable.

Note:  Serial printers must be connected to the serial port. You can enable the parallel port and choose the IRQ through BIOS Setup on page 30 “Onboard Parallel Port”.

Serial port COMA and COMB Connector (Two 10-pin blocks): J2, J3

These connectors support the provided serial port ribbon cables with mounting bracket.  Connect the ribbon cables to these connectors and mount the bracket to the case on an open slot.  The two serial ports on the mounting bracket will then be used for pointing devices or other serial devices.  See page 30 for BIOS configuration of “Onboard Serial Port”

Floppy drive Connector (34-pin block): FLOPPY (J6)

This connector supports the provided floppy drive ribbon cable.  After connecting the single end to the board, connect the two plugs on the other end to the floppy drives.

Primary IDE Connector (40-pin block): PRI (J5)

This connector supports the provided IDE hard disk ribbon cable.  After connecting the single end to the board, connect the two plugs at the other end to your hard disk(s).  If you install two hard disks, you must configure the second drive to Slave mode by setting its jumpers accordingly.  Please refer to the documentation of your hard disk for the jumper settings.  See the figure below.

Secondary IDE Connector (40-pin block): SEC (J4)

This connector able to connect second set of Master and Slave hard disks.  Follow the same procedure described for the primary IDE connector. You may also need to configure two hard disks as one for Masters and other for slave using one ribbon cable.

Turbo Switch: TBSW

Turbo LED switch: TBLED

The motherboard‘s turbo function is always on. The turbo LED connection is labeled here but the LED will remain constantly lit while the system power is on.  You may wish to connect the Power LED from the system case to this lead.

Keyboard lock switch lead: KEYLOCK

This 5-pin connector connects to the case-mounted key switch for locking the keyboard for security purposes.

Speaker connector: SPEAKER

This 4-pin connector connects to the case-mounted speaker.

Reset switch lead: RESET

This 2-pin connector connects to the case-mounted reset switch for rebooting your computer without having to turn off your power switch. This is a preferred method of rebooting in order to prolong the life of the system‘s power supply.

IR connector: IR

SMI suspend switch lead: SMI

This allows the user to manually place the system into a suspend mode or “Green” mode where system activity will be instantly decreased to save electricity and expand the life of certain components when the system is not in use. This 2-pin connector (see the figure below) connects to the case-mounted suspend switch.  If you do not have a suspend switch on your case, you may use the “Turbo Switch” connector connects to SMI suspend switch. SMI is activated when it detects a short to open therefore leaving it shorted will not cause any problems. At first time may require one or two pushes depending on the position of the switch. Wake-up function can be controlled by settings in the BIOS or by press any key from the keyboard (SMI lead cannot wake-up the system). If you want to use this connector “Suspend Switch”, in the POWER MANAGEMENT SETUP of the BIOS software should be change setting to Enable.

Selections			SMI

Enter suspend mode	short

Normal			open

IDE activity LED: IDELED

This connector connects to the hard disk activity indicator light on the case.

Chapter 3

AWARD BIOS SETUP

Award's ROM BIOS provides a built-in Setup program which allows user modify the basic system configuration and hardware parameters.  The modified data will be stored in a battery-backed CMOS RAM so data will be retained even when the power is turned off. In general, the information saved in the CMOS RAM stay unchanged unless here is configuration change in the system, such as hard drive replacement or new equipment is installed.

It is possible that CMOS had a battery failure which cause data lose in CMOS_RAM. If so, re_enter system configuration parameters become necessary.

To enter Setup Program

Power on the computer and press <Del> key immediately will bring you into BIOS CMOS SETUP UTILITY.

ROM PCI/ISA BIOS (2A59GJ19)

CMOS SETUP UTILITY

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

STANDARD CMOS SETUP

BIOS FEATURES SETUP

CHIPSET FEATURES SETUP

POWER MANAGEMENT SETUP

PNP/PCI CONFIGURATION

LOAD BIOS DEFAULTS

LOAD SETUP DEFAULTS

INTEGRATED PERIPHERALS

SUPERVISOR PASSWORD

USER PASSWORD

IDE HDD AUTO DETECTION

HDD LOW LEVEL FORMAT

SAVE & EXIT SETUP

| EXIT WITHOUT SAVING |  |
| --- | --- |

Esc : QUIT                       ô¡õ¡÷¡ö¡   : Select Item

| F10 : Save & Exit Setup (Shift) F2 : Change Color |  |  | Time, Date, Hard Disk Type... |  |  |
| --- | --- | --- | --- | --- | --- |

Figure 3-1

The menu displays all the major selection items and allow user to select any one of shown item.  The selection is made by moving cursor (press any direction key) to the item and press <Enter> key.  An on_line help message is displayed at the bottom of the screen as cursor is moving to various items which provides user better understanding of each function.  When a selection is made, the menu of selected item will appear so the user can modify associated configuration parameters.

3-1  STANDARD CMOS SETUP

Choose "STANDARD CMOS SETUP" in the CMOS SETUP UTILITY Menu (Figure 3-1).  The STANDARD CMOS SETUP allows user to configure system setting such as current date and time, type of hard disk drive installed in the system, floppy drive type, and the type of display monitor.  Memory size is auto-detected by the BIOS and displayed for your reference.  When a field is highlighted (direction keys to move cursor and <Enter> key to select), the entries in the field will be changed by pressing <PgDn> or <PgUp> keys or user can enter new data directly from the keyboard.

ROM PCI/ISA BIOS (2A59GJ19)

STANDARD CMOS SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Date (mm:dd:yy) : Fri, Jul, 12  1996

Time (hh:mm:ss) : 18 : 45 : 18

HARD DISKS         TYPE  SIZE  CYLS  HEAD  PRECOMP  LANDZ  SECTOR  MODE

Primary Master   : Auto     0     0     0        0      0       0  Auto

Primary Slave    : Auto     0     0     0        0      0       0  Auto

Secondary Master : Auto     0     0     0        0      0       0  Auto

Secondary Slave  : Auto     0     0     0        0      0       0  Auto

Drive A : 1.2M , 5.25 in.

Drive B : None

Video   : EGA/VGA

Halt On : All Errors

Base  Memory :   640K

Extended  Memory :  7168K

Other  Memory :   384K

| Total Memory : 8192K |  |
| --- | --- |

Esc : Quit             ô¡õ¡÷¡ö¡ : Select Item        Pu/Pd/+/- : Modify

| F1 : Help (Shift)F2: Change Color |  |  |
| --- | --- | --- |

Figure 3-2

NOTE:	If hard disk Primary Master/Slave and Secondary Master/Slave were   used Auto, than the hard disk size and model will be auto-detect on display during POST.

NOTE:	The "Halt On:" field is to determine when to halt the system by the BIOS is error occurred during POST.

3-2   BIOS FEATURES SETUP

Select the "BIOS FEATURES SETUP" option in the CMOS SETUP UTILITY menu allows user to change system related parameters in the displayed menu.  This menu shows all of the manufacturer's default values of J-656VXD/J-656VXDP.  Again, user can move the cursor by pressing direction keys and <PgDn> of <PgUp> keys to modify the parameters.  Pressing [F1] key to display help message of the selected item.

This setup program also provide 2 convinent ways to load the default parameter data from BIOS [F6] or CMOS [F7] area if shown data is corrupted.  This provides the system a capability to recover from any possible error.

ROM PCI/ISA BIOS (2A59GJ19)

BIOS FEATURES SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Virus Warning              : Disabled

CPU Internal Cache         : Enabled

External Cache             : Enabled

Quick Power On Self Test   : Disabled

Boot Sequence              : A,C

Swap Floppy Drive          : Disabled

Boot Up Floppy Seek        : Enabled

Boot Up Numlock Status     : On

Boot Up System Speed       : High

Gate A20 Option            : Fast

Memory Parity Check        : Disabled

Typematic Rate Setting     : Disabled

Typematic Rate (Chars/Sec) : 6

Typematic Delay (Msec)     : 250

Security Option : Setup

Video  BIOS Shadow      : Enabled

C8000-CBFFF Shadow      : Disabled

CC000-CFFFF Shadow      : Dsiabled

D0000-D3FFF Shadow      : Disabled

D4000-D7FFF Shadow      : Disabled

D8000-DBFFF Shadow      : Disabled

DC000-DFFFF Shadow      : Dsiabled

PCI/VGA Palette Snoop      : Disabled

OS Select For DRAM > 64MB  : Non-OS2

Esc: Quit    ô¡õ¡÷¡ö¡  : Select Item

F1 : Help           Pu/Pd/+/-:Modify

F5 : Old Values    (Shift)F2 : Color

F6 : Load BIOS Defaults

| F7 : Load Setup Defaults |  |
| --- | --- |

Figure 3-3

Note:	The Security Option contians "setup" and "system". The "setup" indicates that the password setting is for CMOS only while the "system" indicates the password setting is for both CMOS and system boot up procedure.

Virus Warning:  This category flashes on the screen.  During and after the system boots up, any attempt to write to the boot sector or partition table of the hard disk drive will halt the system and the following error message will appear, in the mean time, you can run an anti-virus program to locate the problem.  Default value is Disabled

Enabled:	Activates automatically when the system boots up causing a        warning message to appear when anything attempts to access the boot sector or hard disk partition table.

Disabled:	No warning message to appear when anything attempts to access the boot sector or hard disk partition table.

CPU Internal Cache / External Cache:  These two categories speed up memory access.  However, it depends on CPU/chipset design.  The default value is Enable.  If your CPU without Internal Cache then this item "CPU Internal Cache" will not be show.

Enabled:	Enable cachehis category speeds up Power On Self Test. 				(POST) after you power on the computer.

Disabled:	Disable cache

Quick Power On Self Test:  If it is set to Enable, BIOS will shorten or skip some check items during POST.

Enabled:	Enable quick POST

Disabled:	Normal POST

Boot Sequence:   This category determines which drive computer searches first for the DOS (Disk Operating System).  Default value is A,C.

A,C:	System will first search for floppy disk drive then hard disk drive.

C,A:	System will first search for hard disk drive then floppy disk drive.

Swap Floppy Drive:  The swap floppy drive.  Default value is Disabled.

Enabled:	Floppy A & B will be swapped under the DOS

Disabled:	Floppy A & B will be not swap

Boot Up Floppy Seek:  During POST, BIOS will determine if the floppy disk drive installed is 40 or 80 tracks.  360K type is 40 tracks while 760K, 1.2M and 1.44M are all 80 tracks.  The default value is Enabled.

Enabled:	BIOS searches for floppy disk drive to determine if it is 40 or 80 tracks.

Note that BIOS can not tell from 720K, 1.2M or 1.44M drive type as they are all 80 tracks.

Disabled:	BIOS will not search for the type of floppy disk drive by track number.

Note that there will not be any warning message if the drive installed is 360K.

Boot Up NumLock Status:  The default value is On.

On:	Keypad is number keys.

Off:	Keypad is arrow keys.

Boot UP System Speed:  It selects the default system speed-the speed that the system will run at immediately after power up.

High:	  Set the speed to high.

Low:	  Set the speed to low.

NOTE: The board default value is LOW in the field. Boot the system to controller turbo or De-turbo by Onboard (Turbo Switch).

Gate A20 Option:  The default value is Fast.

Normal:	The A20 signal is controlled by keyboard controller or chipset hardware.

Fast:	Default: Fast. The A20 signal is controlled by Port 92 or chipset specific method.

Typematic Rate Setting:  This determines the typematic rate.

Enabled:	Enable typematic rate and typematic delay programming.

Disabled:	Disable typematic rate and typematic delay programming. The system BIOS will use default value of this 2 items and the default is controlled by keyboard.

Typematic Rate (Chars/Sec):

6  :   6  characters per second		  8	:   8  characters per second

10  :  10  characters per second	 	 12	:  12  characters per second

15  :  15  characters per second	 	 20	:  20  characters per second

24  :  24  characters per second	 	 30	:  30  characters per second

Typematic Delay (Msec):  When holding a key, the time between the first and second character displayed.

250  :   250 msec

500  :   500 msec

750  :   750 msec

1000  :  1000 msec

Security Option:  This category allows you to limit access to the system and Setup, or just to Setup.  The default value is Setup.

System:	The system will not boot and access to Setup will be denied if the correct password is not entered at the prompt.

Setup:	The system will boot, but access to Setup will be denied if the incorrect password is entered at the prompt.

NOTE:  	To disable security, select PASSWORD SETTING at Main Menu and then you will be asked to enter password. Do not type anything and just press <Enter>, it will disable security.  Once the security is disabled, the system will boot and you can enter Setup freely.

Video BIOS Shadow:  It determines whether video BIOS will be copied to RAM, however, it is optional from chipset design. Video Shadow will increase the video speed.

Enabled:	  Video shadow is enabled

Disabled:	  Video shadow is disabled

C8000 - CBFFF	Shadow:

CC000 - CFFFF 	Shadow:

D0000 - D3FFF	Shadow:

D4000 - D7FFF	Shadow:

D8000 - DBFFF	Shadow:

DC000 - DFFFF 	Shadow:

These categories determine whether optional ROM will be copied to RAM by 16K byte or 32K byte per/unit and the size depends on chipset.

Enabled:	Optional shadow is enabled.

Disabled:	Optional shadow is disabled.

3-3   CHIPSET FEATURES SETUP

Choose the "CHIPSET FEATURES SETUP" in the CMOS SETUP UTILITY menu to display following menu.

ROM PCI/ISA BIOS (2A59GJ19)

CHIPSET FEATURES SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Auto Configuration       : Enabled

DRAM Timing              : 70 ns

DRAM RAS# Precharge Time : 4

DRAM R/W Leadoff Timing  : 6

DRAM RAS To CAS Delay    : 3

DRAM Read Burst (EDO/FP) : x222/x333

DRAM Write Burst Timing  : x333

Fast MA to RAS# Delay CLK: 2

Fast EDO Path Select     : Disabled

Refresh RAS# Assertion   : 5 Clks

ISA Bus Clock            : PCICLK/4

SDRAM (CAS Lat/RAS-to-CAS: 3/3

System BIOS Cacheable    : Disabled

Video BIOS Cacheable     : Disabled

8 Bit I/O Recovery Time  : 1

16 Bit I/O Recovery Time : 1

Memory Hole At 15M-16M   : Disabled

Peer Concurrency : Enabled

Esc: Quit     ô¡õ¡÷¡ö¡: Select Item

F1 : Help          Pu/Pd/+/-:Modify

F5 : Old Values   (Shift)F2 : Color

F6 : Load BIOS Defaults

| F7 : Load Setup Defaults |  |
| --- | --- |

Figure 3-4

DRAM Timing:  The default value is 60ns.

60ns	: 2 (faster) Burst Wait State, for 60~70ns Fast Page Mode/EDO DRAM.

70ns	: 3 (slower) Burst Wait State, for 70ns Fast Page Mode/EDO DRAM.

Video BIOS Cacheable:  The default value is Enabled.

Enabled:	This field Enabled the Video BIOS Cacheable to speed up to VGA Performance.

Disabled:	Disabled the Video BIOS Cacheable function.

8/16 Bit I/O Recovery Time:  The default value is 1.

8 Bit I/O Recovery Time:	This field defines the recovery time from 1 to 8

for 8-bit I/O.

16 Bit I/O Recovery Time:	To define the recovery time from 1 to 4 for 16-bit

I/O.

Memory Hole At 15M~16M:The default value is Disabled.

Disabled:	Normal Setting.

Enabled:	This field enableds the main memory (15~16MB) remap to ISA BUS.

3-4   POWER MANAGEMENT SETUP

Choose the "POWER MANAGEMENT SETUP" in the CMOS SETUP UTILITY  to display the following screen. This menu allows user to modify the power management parameters and IRQ signals. In general, these parameters should not be changed unless it's absolutely necessary.

ROM PCI/ISA BIOS (2A59GJ19)

POWER MANAGEMENT SETUP

| AWARD SOFTWARE, INC. |  |  |
| --- | --- | --- |

Power Management    : Disabled

PM Control by APM   : Yes

Video Off Method    : V/H SYNC+Blank

Doze Mode           : Disabled

Standby Mode        : Disabled

Suspend Mode        : Disabled

HDD Power Down      : Disabled

** Wake Up Events In Doze & Standby **

IRQ3 (Wake-Up Event): ON

IRQ4 (Wake-Up Event): ON

IRQ8 (Wake-Up Event): ON

IRQ12(Wake-Up Event): ON

** Power Down & Resume Events **

IRQ3 (COM 2)         : ON

IRQ4 (COM 1)         : ON

IRQ5 (LPT 2)         : OFF

IRQ6 (Floppy Disk)   : OFF

IRQ7 (LPT 1)         : OFF

IRQ8 (RTC Alarm)     : OFF

IRQ9 (IRQ2 Redir)    : OFF

IRQ10 (Reserved)     : OFF

IRQ11 (Reserved)     : OFF

IRQ12 (PS/2 Mouse)   : OFF

IRQ13 (Coprocessor)  : OFF

IRQ14 (Hard Disk)    : ON

IRQ15 (Reserved)     : OFF

Esc: Quit      ô¡õ¡÷¡ö¡: Select Item

F1 : Help          Pu/Pd/+/-: Modify

F5 : Old Values   (Shift)F2 : Color

F6 : Load BIOS Defaults

| F7 : Load Setup Defaults |  |
| --- | --- |

Figure 3-5

Again, user can move the cursor by pressing direction keys to the field need to be modified and press <PgDn> or <PgUp> to alter item selection. You can only change the content of Doze Mode, Standby Mode, and Suspend Mode when the Power Management is set to 'User Define'.

3-4-1   The Description of the Power Management

Power Management mode selection:

Disabled:	The system operates in NORMAL conditions (Non-GREEN), and the Power Management function is disabled.

Max.saving:	This mode will maximize the power saving capability.

Min.saving:	This mode will minimize the power saving capability.

User define:	Allow user to define timeout parameters to control power saving timing.  Refer item shown below:

Timeout parameters:

HDD Standby

HDD Standby timer can be set from 1 to 15 minute(s).

System Doze

The "System Doze" mode timer starts to count when there is no "PM events" occurred.  The valid timeout setting is from 1 minute up to 1 hour.

System Standby

The "Standby" mode timer starts to count when "System Doze" mode timer timed out and no "PM events" occurred.  Valid range is from 1 minute up to 1 hour.

System Suspend

This function works only when the Pentium CPU is installed.  The timer starts to count when "System Standby" mode timer timed out and no "PM Events" occurred.  Valid range is from 1 minute up to 1 hour.

3-4-2   Description of the Green Functions

The J-656VXD/J-656VXDP supports HDD Power Down, Doze and standby power saving functions when Intel Pentium Processor CPU is installed. The suspend function is also supported when the SMI switch is short (ref. page 15). The detail description of these functions are provided as following:

HDD Standby Mode

When system stop reading or writing HDD, the timer starts to count.  The system will cut off the HDD power when timer ran out of time.  The system

# Text boxes

Keyboard Connector (5-pin female)

Connector Plug from Keyboard

Load BIOS Default (Y/N)? Y

Load SETUP Default (Y/N)? Y

Select Secondary Slav