Enterprise Server Group

Intel M440LX DP Server

Technical Product Specification

Order Number xxxxxx-xxx

Version 0.8

Preliminary

June 30, 1997

The M440LX baseboard may contain design defects or errors known as errata.  Characterized errata that may cause the M440LX baseboard’s behavior to deviate from published specifications are documented in the M440LX Board Set Specification Update.

Revision History

| Revision | Revision History | Date |
| --- | --- | --- |
| Rev 0.8 | Preliminary release of the M440LX DP Server Board Set Technical Product Specification | 6/97 |

This product specification applies only to standard M440LX DP Server board set with BIOS identifier DM0.  Information in this version of the summary applies to the BIOS 1.00.01 DM0.  Different versions of the BIOS may look and behave differently.

Changes to this summary will be published in the M440LX DP Server Board Set Specification Update before being incorporated as a revision to this document.

Note:  If printing this document from an electronic file, use a PostScript printer with the appropriate PostScript print driver to insure the drawings print clearly.

Information in this document is provided in connection with Intel products. No license, express or implied, by estoppel or otherwise, to any intellectual property rights is granted by this document. Except as provided in Intel's Terms and Conditions of Sale for such products, Intel assumes no liability whatsoever, and Intel disclaims any express or implied warranty, relating to sale and/or use of Intel products including liability or warranties relating to fitness for a particular purpose, merchantability, or infringement of any patent, copyright or other intellectual property right. Intel products are not intended for use in medical, life saving, or life sustaining applications. Intel may make changes to specifications and product descriptions at any time, without notice.

Technical updates should be obtained by calling Intel Literature or writing:

Intel Corporation
	P.O. Box 7641
	Mt. Prospect, IL 60056-7641

or call in North America 1-800-879-4683, Europe 44-0-1793-431-155, France 44-0-1793-421-777,
	Germany 44-0-1793-421-333, Japan (fax only) 81-0-120-478-832, other Countries 708-296-9333

†	Third-party brands and trademarks are the property of their respective owners.

Copyright  1996, Intel Corporation.  All rights reserved

Table of Contents

1.	Board Set Descriptions	2

1.1	Product Overview	2

1.2	Performance	2

1.3	Baseboard	2

Baseboard Diagram	5

Processor/PCI Host Bridge/Memory Subsystem	5

PCI I/O Subsystem (PCI-P)	8

Secondary PCI I/O Subsystem (PCI-S)	12

ISA I/O Subsystem	14

System Reset Control	15

Clock Generation and Distribution	16

Interrupts and I/O APIC	17

Baseboard Jumper Settings	21

1.4	EDO Memory Module	22

EDO DRAM Array	22

1.5	RPX Module	24

Battery Backup	25

2.	Server Management	27

2.1	Baseboard Management Controller (BMC)	28

Fault Resilient Booting	29

2.2	Front Panel Controller (FPC)	29

2.3	I2C Isolation Buffers and Auxiliary I2C Connector	30

2.4	Madrona Interrupt Steering and Server Management Interface Chip (MISSMIC)	30

2.5	System Fan Interface	30

3.	Memory and Other Resource Mappings	32

3.1	Extended Memory	32

3.2	I/O Map	33

3.3	Device Number and IDSEL Mapping	37

4.	BIOS, Setup, SCU and SCSI Utility	38

4.1	BIOS Overview	38

4.2	System BIOS	39

5.	Boardset Specifications	40

5.1	Absolute Maximum Ratings	40

5.2	Electrical Specifications	40

Power Connection	41

Figures

Figure 1 M440LX DP Server Functional Block Architecture	4

Figure 2 M440LX Baseboard Layout	5

Figure 3 Processor/PCI Host Bridge/Memory Subsystem	6

Figure 4 Reset Flow Diagram	15

Figure 5 M440LX Server Baseboard Clock Distribution	16

Figure 6 Memory Module Layout	22

Figure 7 M440LX EDO Memory module  Block Diagram	23

Figure 8 RPX Module Diagram	24

Figure 9 Battery Backup Block Diagram	25

Figure 10 M440LX Server Management Architecture	28

Figure 11 Extended Memory Map	32

Figure 12 M440LX BIOS Architecture	38

Tables

Table 1 Standard VGA Modes	11

Table 2 Extended VGA Modes	12

Table 3 PCI-S Configuration IDs	13

Table 4 M440LX Interrupt StructureInterrupt Routing	19

Table 5 PCI-P Interrupt Routing	19

Table 6 PCI-S Interrupt Routing	19

Table 7 Interrupt Definitions	20

Table 8 Configuration Jumpers	21

Table 9 Configuration Jumper Options	21

Table 10 Tachometer Fan Connector Pinout	30

Table 11 Fansink Connector Pinout	31

Table 12 M440LX I/O Map	33

Table 13 PCI Configuration IDs and Device Numbers	37

Table 14 Absolute Maximum Ratings	40

Related Documentation

Balboa II Chassis TPS

M440LX DP Server Performance Report

M440LX DP Server Product Guide

Symbios SDMS 4.0 User Guide

BM440LX DP Server system Data Sheet

MTA Testview User’s Guide

1.1

1.		Board Set Descriptions

1.1	Product Overview

The M440LX DP Server is a high performance dual Pentium® II processor based server using the DT82440LX PCI chip set. The M440LX architecture extends across multiple Pentium Pro processor generations, and evolves intelligent I/O technology to meet their I/O demands. The M440LX baseboard provides a PCI-based I/O subsystem containing embedded devices for video and disk control, along with ISA bus support for legacy devices.  The baseboard also provides server management and monitoring hardware support, interrupt control (I/O APIC and PC/AT compatible), and intelligent I/O via an embedded i960® I/O processor.

The M440LX baseboard provides the following features:

·	Volume server or desktop platform able to support one or two Pentium® II processors.

·	Dual Pentium II or Deschutes DT processor cards

·	82440LX PCI/AGP Controller (PAC) as PCI host bridge and memory controller

·	Support for EDO DRAM or SDRAM memory module via edge connector interface

·	Primary PCI segment (PCI-P) with three expansion connectors and four embedded devices. 960RD Bridge and I/O controller, PIIX4, Cirrus Logic GD54M40 SVGA Video, and Symbios SYM53C810 narrow SCSI controller.

·	Secondary PCI segment (PCI-S) with four expansion connectors (one physically shared with an ISA slot) and two wide Ultra SCSI controllers - Symbios SYM53C875.

·	Support for Intelligent I/O (I2O) on PCI-S.

·	ISA bus segment with three expansion connectors (one physically shared with PCI-S).

·	Server management microcontrollers providing monitoring, alerting, and logging of critical system information obtained from embedded sensors on baseboard.

1.2	Performance

1.3	Baseboard

The M440LX baseboard supports up to two Pentium II (or Deschutes DT) processor cards.  The baseboard provides two “Slot 1” connectors, with an embedded VRM 8.1-compliant voltage regulator (DC-to-DC converter) for connector 0, and plug-in VRM support for connector 1.  The 82440LX PCI/AGP controller (PAC) device provides the 32-bit address/64-bit data processor host bus interface, operating at 66 MHz in the GTL+ signaling environment.  The PAC contains a 32-bit PCI host bridge to a 33 MHz 5V PCI 2.1 signaling environment.  The PAC also acts as memory controller and data path controller for the system. The ECC implementation in the PAC can detect and correct single-bit errors, and detect multiple-bit errors.  The PAC also contains an AGP interface, which is unused on M440LX, and not discussed in this document.

M440LX system architecture is partitioned such that the processor SEC cartridges, memory module, ISA/PCI add-in cards, and peripherals plug into the baseboard.  The I/O subsystem also provides connector interfaces to the system front panel, standard ISA peripherals (e.g., floppy, IDE, keyboard, mouse), hot-swap SCSI backplane, and power supply sharing subsystem.  In addition, baseboard connector interfaces that support ISA and PCI standard add-in cards are provided.  Two PCI I/O segments on the baseboard: PCI-P (primary PCI segment directly under the host bridge), and PCI-S (secondary I/O segment under PCI-to-PCI bridge) contain embedded devices and slots

Three onboard PCI SCSI controllers reside in the I/O subsystem.  The primary PCI segment provides a single narrow (8-bit) SCSI controller, and the secondary segment (under the I2O bridge) provides two Ultra SCSI controller devices.  As PCI 2.1 bus masters, each SCSI controller supports burst data transfers up to the maximum rate of 133 MB/s on PCI.  It is intended that only wide, (16-bit), target devices be attached to the two Ultra SCSI interfaces, and that legacy 8-bit peripherals be attached to the narrow SCSI interface.

Figure 1 M440LX DP Server Functional Block Architecture

Baseboard Diagram

The following diagram shows the placement of major components and connector interfaces on the M440LX baseboard.

0

Figure 2 M440LX Baseboard Layout

Processor/PCI Host Bridge/Memory Subsystem

The processor/PCI bridge/memory subsystem consists of one to two identical Pentium Pro processor cards, a plug-in memory board, and support circuitry on the baseboard consisting of the following:

·	Intel 440LX PCI/AGP Controller (PAC) PCI host bridge and memory controller

·	Dual “Slot 1” edge connectors that accept the Pentium II or Deschutes DT processor cards

·	242-pin connector interface to memory board, which contains clock generation circuitry

·	Processor host bus GTL+ support circuitry, including termination power supply

·	Embedded DC-to-DC voltage converter for processor card 0 power; socket for plug-in VRM for processor card 1 power

·	APIC bus

·	Miscellaneous logic for reset configuration, processor card presence detection, ITP port, and server management

Figure 3 Processor/PCI Host Bridge/Memory Subsystem

Pentium II Processor Card

M440LX is designed to accommodate the Pentium II processor card from 233Mhz to 300Mhz.  Unlike its predecessor, in which the processor core/L1 cache and L2 cache are housed in dual-cavity PGA packaging, the Pentium II processor core/L1 cache appears on one side of a pre-assembled printed circuit board, approximately 2.5" x 5" in size, with the L2 cache on the backside.  This assembly is referred to as a processor card.

The L2 cache and processor core/L1 cache connect using a private bus isolated from the processor host bus.  This Pentium II L2 cache bus operates at half of the processor core frequency.  To compensate for the cache bus speed, the internal L1 data and code caches have been enlarged to 16 KB, double the size of its predecessor.

As with previous versions of Pentium Pro processors, the Pentium II processor card external interface is designed to be MP-ready.  Each processor contains a local APIC section for interrupt handling.  When two processor cards are installed, the pair of processor cards must be of identical revision, core voltage, and bus/core speeds.

Retention Module

Processor Card Connector

The Pentium II processor card edge connector conforms to the “Slot 1” specification, which can also accommodate future processor cards. The processor modules connectors are also known as Single Edge Connector (SEC). The baseboard provides 2 connectors. The processors face towards the memory module.

Processor Bus Termination/Regulation/Power

The termination circuitry required by the Pentium Pro processor bus (GTL+) signaling environment, and the circuitry to set the GTL+ reference voltage are implemented directly on the processor cards.  The baseboard provides 1.5V GTL+ termination power (VTT), and VRM 8.1-compliant DC-to-DC converters to provide processor power (VCCP) at each connector.  Power for processor 0 is derived from the 12V supply, using an embedded DC-DC converter onboard.  A socket is provided on the baseboard for a VRM to power processor 1, which derives power from the 5V supply.

Termination Card

If only one processor card is installed in a system, a termination card must be installed in the vacant processor card slot to ensure reliable system operation.  The termination card contains  GTL+ termination circuitry, clock signal termination, and Test Access Port (TAP) bypassing for the vacant connector.

APIC Bus

Interrupt notification and generation for the processors is done using an independent path between local APICs in each processor and the Intel I/O APIC located on the baseboard.  This simple bus consists of 2 data signals and one clock line.  Refer to “I/O APIC and Interrupts” later in this chapter for more information.

440LX Host Bridge

The 82440LX PCI/AGP Controller (PAC) is the host bridge between the Pentium II ® processors and I/O systems.  The 440LX PAC is a 492-pin ball-grid array (BGA) device that performs control signal translations and manages the data path.  The host bridge in the PAC supports one or two processors at a processor host bus frequency of 66 MHz, with 32-bit addressing, optimized in-order and request queue (IOQ), and dynamic deferred transaction support.  The GTL+ host bus connects the processor card with other resources in the system through the 440LX PAC host bridge.  The host bridge translates 64-bit operations in the GTL+ signaling environment at 66 MHz to a 32-bit PCI I/O subsystem. The 440LX PAC also handles arbitration for the primary PCI bus.

The PCI interface provides greater than 100 MB/s data streamlining for PCI to DRAM accesses, while supporting concurrent processor host bus and PCI transactions to main memory. This is accomplished using extensive data buffering, with processor-to-DRAM and PCI-to-DRAM write data buffering and write-combining support for processor-to-PCI burst writes.  Five PCI masters can be supported in addition to the host processor(s) and PCI to ISA bridge functions.

The 440LX PAC also contains the memory controller for M440LX.  Memory amounts from 8 MB to 1 GB of DIMM are possible, with a 64/72-bit non-interleaved pathway to main memory, which is located on a plug-in module. The memory controller supports SDRAM and EDO DRAMs. System clock generation is located on the memory module due to the significantly different clock requirements of EDO and SDRAM memory.

ECC is provided which can detect and correct single-bit errors (SED/SEC), and detect all double-bit and some multiple-bit errors (DED).  Under software control, you may configure parity checking, and the level of ECC desired.  On power-up ECC and parity checking are disabled.

PCI I/O Subsystem (PCI-P)

The M440LX server is designed with two PCI bus segments: the primary (PCI-P) and the secondary (PCI-S). Each segment is compliant with revision 2.1 of the PCI specification operating at 33 MHz.  PCI-P is the primary PCI segment, produced by the PCI interface from the 440LX PAC.  The secondary PCI segment, PCI-S, operates through the PCI-to-PCI bridge in the i960RD, in a hierarchical bus structure.  The two hierarchical PCI segments run concurrently with the processor bus and with each other increasing throughput through independent arbitration and data buffering.  A total of seven PCI slots for add-in cards, (three on PCI-P, and four on PCI-S) are available.  A single PCI slot on the secondary segment is physically shared with an ISA slot.  The first PCI-S slot supports a half-length PCI card when the RPX module is installed.  All other PCI slots support full-length cards.

All I/O is directed through the primary PCI bus segment. The primary PCI I/O bus includes: 3 PCI slots (P0, P1, and P2), the i960 RD PCI-to-PCI bridge to the secondary PCI I/O bus, the Intel PIIX4 controller, the Cirrus Logic CL-GD54M40 SVGA video controller, and the Symbios 53M810 narrow SCSI controller.

PCI-0 Arbitration

Because the primary PCI bus supports six PCI masters (slots P0 through P2, i960 RD, SCSI, PIIX4, and PAC) and one slave, all PCI masters must arbitrate for PCI access. The 440LX PAC accomplishes this.  Note that the PCI video is a slave only device

PCI-to ISA/IDE/USB Controller (PIIX4)

The PIIX4 provides 4 specific PCI functions in a single package, PCI-to-ISA bridge, IDE interface, USB controller (not used on the M440LX), and power management controller.  Each of the 4 functions in the PIIX4 contain its own set of configuration registers that appear to the M440LX system as a unique hardware controller sharing the same PCI bus interface.

The PIIX4 is packaged as a 324-pin BGA device

The PIIX4 fully implements a 32-bit PCI master/slave interface, in accordance with the PCI Local Bus Specification, Rev. 2.1.  The PCI interface operates at 33 MHz, using the 5V-signaling environment.

The PIIX4 provides an ISA bus interface, operating at 8.33 MHz, that supports 3 ISA connectors, Flash memory, server management interface, and the National Super I/O chip.

The Fast IDE controller in the PIIX4 supports programmed I/O transfers up to 14 MB/s and bus master IDE transfers up to 32 MB/s.  The PIIX4 supports two IDE channels but the M440LX baseboard only utilizes the primary IDE channel.  The single IDE connector, featuring 40 pins (2 x 20), is provided on the baseboard.

i960 RD PCI-to-PCI Bridge

The i960 RD is a high performance 80960JF core processor running at 66 MHz that provides the PCI-to-PCI bridge from the Primary PCI bus to the Secondary PCI bus on M440LX. This Bridge is compliant with the PCI 2.1 specification.  The i960RD also provides an Integrated memory controller unit, a Multi-channel DMA controller, and an I2C bus interface unit.  The i960RD also has a secondary PCI bus arbitration unit.

RP Expansion (RPX) Card Interface

The M440LX baseboard provides a connector interface to modular local memory for the 80960JF processor in the i960 RD: the RPX connector.  The RPX card for M440LX attaches to this interface, which contains local memory, and firmware support for intelligent I/O (I2O) operations. The RPX card can also be used for on board RAID using the two Symbios SYM53C875 Ultra SCSI controllers on the Secondary PCI segment. The RPX connector provides additional signals in anticipation of future upgrades. Refer to the RPX Module section for more Information

PCI-P Narrow SCSI

A narrow SCSI host adapter, Symbios SYM53C810, is integrated into the server baseboard.  The SYM53C810 contains a high performance SCSI core capable of Fast 8-bit SCSI transfers in single-ended mode.  The high performance SCSI core, PCI bus master DMA, and internal SCRIPTS™ processor all meet SCSI-1 and SCSI-2 standards. The 100-pin PQFP packaged component provides programmable active negation, PCI zero wait-state bursts of faster than 110 MB/s @ 33 MHz, and SCSI transfers rates from 5 MB/s to 10 MB/s.

The device also offers active negation outputs.  Active negation outputs reduce the chance of data errors by actively driving both polarities of the SCSI bus, avoiding indeterminate voltage levels and common-mode noise on long cable runs.  The SCSI output drivers can directly drive a 48 mA single-ended SCSI bus with no additional drivers.

The SCSI data bus is 8-bits wide with even or odd parity generation.  The SYM53C810 has a very flexible parity scheme allowing both parity senses, the ability to disable parity, and the ability to generate bad parity for testing whether errors are handled correctly.  The SYM53C810 supports variable block size and scatter/gather data transfers.  It supports a SCRIPTS™ language for high performance, flexibility, and ease of use.  The SYM53C810 performs complex bus sequences without interrupts, including restore data pointers

SYM53C810 PCI Signals

The SYM53C810 supports all of the required 32-bit PCI signals including the PERR_L and SERR_L functions.  Full PCI parity is maintained on the entire data path through the SYM53C810 SCSI controller.

The extensions to memory commands (memory read multiple, memory read line, and memory write and invalidate) work with the cache line size register to give the cache controller advance knowledge of the minimum amount of data to expect.  The decision to use either the memory read line or memory read multiple commands is determined by bits in the configuration space command register for this device, and if correct conditions exist for the particular transfer.

PCI Video

M440LX has a Cirrus Logic CL-GD54M40 integrated video controller and support circuitry on the primary PCI bus.  The CL-GD54M40 32-bit VGA Graphics Accelerator chip contains a SVGA video controller, Clock Generator, and 80 MHz RAMDAC in a 160-pin PQFP.  Standard video memory consists of a single 256 K x 16 DRAM chip providing 512 KB of 60 ns video memory, with optional expansion to 1 MB for improved performance and more video modes.  The 54M40 supports a variety of modes: up to 1280 x 1024 resolution, and up to 64 K colors.

This SVGA subsystem supports analog VGA monitors, single and multi-frequency, interlaced and non-interlaced, up to 87 Hz vertical retrace frequency.  The connector is a standard 15 pin VGA connector.

The CL-GD54M40 supports a minimal set of 32-bit PCI signals since it never acts as a PCI master.  As a PCI-P slave, the device requires no arbitration or interrupt connections.

Video Modes

The 54M40 provide all standard IBM VGA modes.  With 512 KB of video memory, the standard M440LX server goes beyond standard VGA support.  The following tables show all supported video modes using 512 KB, as well as 1 MB of video memory.  The additional 512 KB is user-installable.  The following tables show the standard and extended modes that the chip supports, including the number of colors and palette size (e.g., 16 colors out of 256 K colors), resolution, pixel frequency, and scan frequencies.

| Mode(s) in Hex | Bits Per Pixel | Colors (number /palette size) | Resolution | Pixel Freq. (MHz) | Horiz. Freq. (KHz) | Vert. Freq. (Hz) |
| --- | --- | --- | --- | --- | --- | --- |
| 0, 1 | 4 | 16/256K | 360 X 400 | 14 | 31.5 | 70 |
| 2, 3 | 4 | 16/256K | 720 X 400 | 28 | 31.5 | 70 |
| 4, 5 | 4 | 4/256K | 320 X 200 | 12.5 | 31.5 | 70 |
| 6 | 4 | 2/256K | 640 X 200 | 25 | 31.5 | 70 |
| 7 | 4 | Mono | 720 X 400 | 28 | 31.5 | 70 |
| D | 4 | 16/256K | 320 X 200 | 12.5 | 31.5 | 70 |
| E | 4 | 16/256K | 640 X 200 | 25 | 31.5 | 70 |
| F | 4 | Mono | 640 X 350 | 25 | 31.5 | 70 |
| 10 | 4 | 16/256K | 640 X 350 | 25 | 31.5 | 70 |
| 11 | 4 | 2/256K | 640 X 480 | 25 | 31.5 | 60 |
| 12 | 4 | 16/256K | 640 X 480 | 25 | 31.5 | 60 |
| 12+ | 4 | 16/256K | 640 X 480 | 31.5 | 37.5 | 75 |
| 13 | 8 | 256/256K | 320 X 200 | 12.5 | 31.5 | 70 |

Table 1 Standard VGA Modes

.

| Mode(s) in Hex | BPP | Colors | Resolution | Pixel Freq. (MHz) | Horiz. Freq. (KHz) | Vert. Freq. (Hz) |
| --- | --- | --- | --- | --- | --- | --- |
| 14, 55 | 8 | 16/256K | 1056 X 400 | 41.5 | 31.5 | 70 |
| 54 | 8 | 16/256K | 1056 X 350 | 41.5 | 31.5 | 70 |
| 58, 6A | 8 | 16/256K | 800 X 600 | 40 | 37.8 | 60 |
| 58, 6A | 8 | 16/256K | 800 X 600 | 49.5 | 46.9 | 75 |
| 5C | 8 | 256/256K | 800 X 600 | 36 | 35.2 | 56 |
| 5C | 8 | 256/256K | 800 X 600 | 40 | 37.9 | 60 |
| 5C | 8 | 256/256K | 800 X 600 | 49.5 | 46.9 | 75 |
| 5D | 8 | 16/256K (interlaced) | 1024 X 768 | 44.9 | 35.5 | 87 |
| 5D | 8 | 16/256K | 1024 X 768 | 65 | 48.3 | 60 |
| 5D | 8 | 16/256K | 1024 X 768 | 75 | 56 | 70 |
| 5D | 8 | 16/256K | 1024 X 768 | 78.7 | 60 | 75 |
| 5F | 8 | 256/256K | 640 X 480 | 25 | 31.5 | 60 |
| 5F | 8 | 256/256K | 640 X 480 | 31.5 | 37.5 | 75 |
| 60* | 8 | 256/256K (interlaced) | 1024 X 768 | 44.9 | 35.5 | 87 |
| 60* | 8 | 256/256K | 1024 X 768 | 65 | 48.3 | 60 |
| 60* | 8 | 256/256K | 1024 X 768 | 75 | 56 | 70 |
| 60* | 8 | 256/256K | 1024 X 768 | 78.7 | 60 | 75 |
| 64* | 16 | 64K | 640 X 480 | 25 | 31.5 | 60 |
| 64* | 16 | 64K | 640 X 480 | 31.5 | 37.5 | 75 |
| 65* | 16 | 64K | 800 X 600 | 36 | 35.2 | 56 |
| 65* | 16 | 64K | 800 X 600 | 40 | 37.8 | 60 |
| 65* | 16 | 64K | 800 X 600 | 49.5 | 46.9 | 75 |
| 66* | 16 | 32K Direct/256 Mixed | 640 X 480 | 25 | 31.5 | 60 |
| 66* | 16 | 32K Direct/256 Mixed | 640 X 480 | 31.5 | 37.5 | 75 |
| 67* | 16 | 32K Direct/256 Mixed | 800 X 600 | 40 | 37.8 | 60 |
| 67* | 16 | 32K Direct/256 Mixed | 800 X 600 | 49.5 | 46.9 | 75 |
| 6C* | 16 | 16/256K (interlaced) | 1280 X 1024 | 75 | 48 | 87 |

Table 2 Extended VGA Modes

* Requires 1 MB video memory option.

For more information refer to the Cirrus Logic CL-GD54M40 Reference Manual, Cirrus Logic CL-GD54M40 Advance Product Bulletin, or http://www.cirrus.com/

Secondary PCI I/O Subsystem (PCI-S)

The i960 RD I/O processor performs the function of PCI-to-PCI bridge on the M440LX, which extends the electrical capacity of primary PCI bus segment to form a secondary PCI segment: PCI-S.  The i960 RD forwards all PCI transactions on the primary PCI segment, that fall within specified address ranges, to the secondary PCI segment. It also transfers all PCI transactions on the secondary PCI segment, that fall within specified address ranges, to PCI-P.  The i960 RD is packaged in a 352-lead Plastic Ball Grid Array (PBGA).

The Secondary PCI bus segment contains four 120-pin, 32-bit PCI expansion slot connectors (S0, S1, S2, and S3), and two Symbios SYM53C875 SCSI-3 Ultra SCSI controllers.

| IDSEL Value | Device |
| --- | --- |
| 16 | SYM53C875 SCSI A |
| 17 | PCI Slot S0 |
| 18 | PCI Slot S1 |
| 19 | PCI Slot S2 |
| 20 | SYM53C875 SCSI B |
| 21 | PCI Slot S3 |

Table 3 PCI-S Configuration IDs

PCI-S Arbitration

Because the Secondary PCI bus handles seven PCI masters: slots S0 through S3, the two Ultra SCSI controllers, and the i960 RD.  All PCI masters must arbitrate for PCI access using resources supplied by the i960 RD PCI-to-PCI bridge.  The i960 RD secondary PCI interface arbitration connections are internal to the device.  The internal arbitration unit parks the i960 RD secondary PCI interface on the bus when no other agent is requesting it.  This maximizes the performance of primary to secondary bus transactions when no other PCI masters own the secondary PCI bus.

Wide SCSI Subsystem

The Secondary PCI bus segment provides two embedded Symbios SYM53C875 Ultra SCSI controllers.  The SYM53C875 supports 8-bit SCSI (10 MB/s or 20 MB/s) or 16-bit Wide SCSI (20 MB/s or 40 MB/s) transfers, in a 169-in BGA package.  The SYM53C875 is a highly integrated PCI-to-SCSI solution containing a high-performance PCI bus interface, DMA controller, internal SCRIPTSTM engine, and a high-performance SCSI bus interface.

The SYM53C875 supports all of the required 32-bit PCI signals including PERR_L and SERR_L.  Full PCI parity is maintained on the entire data path through the chip. The SYM53C875 does not support the CLKRUN_L, LOCK_L, SBO_L, SDONE_L and TRST_L signals.  Support for these signals is specified as optional under the PCI 2.1 Specification.

PCI performance features include bursts of up to 128 Dwords for data rates of greater than 110 MB/s.  The SCRIPTS engine is a special high-speed processor optimized for SCSI protocol.  The SCRIPTS engine and 4 KB of internal RAM for instruction storage can execute complex SCSI bus sequences independently of the host processor.  The internal DMA, in combination with the SCRIPTS engine, creates a tightly coupled connection between PCI and SCSI bus interfaces for optimum performance.

SCSI Interface

The SYM53C875 offers 8-bit or 16-bit SCSI operation at data transfer rates of 10, 20, or 40 MB/s. The SYM53C875 uses Tolerant technology for improved data integrity when running in the fastest SCSI transfer modes. Tolerant technology includes active negation of SCSI signals when driving and programmable input signal filtering when receiving. Active negation outputs reduce the chance of data errors by actively driving both polarities of the SCSI bus avoiding indeterminate voltage levels and common-mode noise on long cable runs.  The SYM53C875 also offers controls for external differential transceivers and a disk activity (LED) output.

The SYM53C875 supports the SCSI-2 8- or 16-bits wide bus with odd parity generated per byte.  SCSI control signals are the same for either bus width.  All SCSI signals are active low. SCSI P-connector cabling connects easily. During chip power-down, all inputs are disabled to reduce power consumption.

ISA I/O Subsystem

The ISA I/O subsystem on M440LX provides three ISA slots and compatibility I/O via the I/O controller chip.  One ISA slot is physically shared with a secondary PCI slot (PCI-S3).  The second of the two dedicated slots (ISA-2) only supports half-length cards. The other two ISA slots support full-length cards.  The ISA bus also supports an embedded I/O APIC, Flash BIOS, and an interface to the server management hardware.  The National PC87307 Super I/O chip, which resides on the ISA bus, supports direct connection of keyboard, mouse, floppy drive, and standard parallel and serial ports.

The ISA I/O subsystem also connects with the I/O APIC and MISSMIC.  The I/O APIC handles interrupts produced by ISA devices for the MP environment.  The MISSMIC is a custom ASIC that provides the host interface to the baseboard server management processor, performs interrupt steering and rerouting, and NMI/SMI error interrupt control

National I/O Controller - Serial, Parallel, Floppy, KB/Mouse

The National 87307 device contains all of the necessary circuitry to control two serial ports, one parallel port, floppy disk, and PS/2-compatible keyboard and mouse.  M440LX provides the connector interface for each.  In addition, the 87307 contains a real-time clock.

Two 9-pin connectors are provided in one stacked 9-pin D-Sub housing for Serial port A and Serial port B. By default port A is physically the top connector, port B is on the bottom. Both ports are compatible with 16550A and 16450, and are relocateable. Each serial port can be set to 1 of 4 different COMx ports, and can be enabled separately.  When enabled, each port can be programmed to generate edge or level sensitive interrupts.  When disabled, serial port interrupts are available to add-in cards.

The 25/15 pin connector stacks the parallel port connector over the VGA connector.  The 87307 provides an IEEE 1284-compliant 25-pin bi-directional parallel port.  BIOS programming of the 87307 registers enable the parallel port, and determine the port address and interrupt.  When disabled, the interrupt is available to add-in cards.

The FDC on the 87307 is functionally compatible with the PC8477, which contains a superset of the floppy disk controllers in the DP8473 and N82077. The baseboard provides the 24 MHz clock, termination resistors, and chip selects.  All other FDC functions are integrated into the 87307 including analog data separator and 16-byte FIFO.

The keyboard and mouse connectors are mounted within a single stacked housing.  The mouse connector is stacked over the keyboard connector.  External to the board they appear as two connectors.  The keyboard and mouse controller is software compatible with the 8042AH and PC87911. The keyboard and mouse connectors are PS/2 compatible.

While the National PC87307 contains a Real Time Clock, The M440LX server baseboard utilizes the RTC in the Intel PIIX4.

System Reset Control

Reset circuitry on the M440LX server baseboard looks at resets from the front panel, PIIX4, I/O controller, and processor subsystem to determine proper reset sequencing for all types of reset.  The reset logic is designed to accommodate a variety of ways to reset the system, either by a Power-up, a hard reset, or a programmed (soft) reset.

The following diagram shows the critical baseboard signals associated with reset.

Figure 4 Reset Flow Diagram

Reset circuitry on the M440LX baseboard looks at resets from the front panel, PIIX4, I/O controller, and processor subsystem to determine proper reset sequencing for all types of reset.

The most common "reset" is the power-up or power-on sequence that must happen to turn on the server system. When a valid input voltage level is provided to the power supply, 5 Volt standby power will be applied to the baseboard.  A power monitor circuit on 5 Volt standby will assert a signal, causing the front panel controller (FPC) to be reset.  The FPC monitors and controls key events in the system related to reset and power control.

A hard reset may be initiated by software, by the user resetting the system through the front panel switch, or through the Server Management Module add-in card.  For software initiated hard reset, Intel recommends using the PIIX4 Reset Control register.

A soft reset causes the processors to begin execution in a known state without flushing cache resources or internal buffers.  Soft resets may be generated by the keyboard controller (located in the 87307), by the Intel PIIX4, or by the Intel 82440LX PAC.

A Programmed Reset may be initiated by software.  Although reset control is provided by registers in the Intel 82440LX PAC, the component documentation recommends that the PIIX4 Reset Control register be used instead for Programmed Resets

Clock Generation and Distribution

There are three clock sources used on the M440LX server baseboard.  The memory module generates the 33.3 MHz PCI reference clock, the 66.6 MHz host clocks, and the 14.318 MHz APIC clocks.  A clock generator on the baseboard generates a 40 MHz clock for the embedded SCSI controllers, a 24 MHz clock for the super I/O, a 16 MHz clock for the BMC, and a 14.318 MHz clock for ISA devices.  The Front Panel Controller has its own crystal, providing a 12 MHz time reference to that microcontroller, since it operates off the 5 V standby.  The baseboard also has a low skew clock buffer to distribute the PCI reference clock to all the embedded PCI devices and to all PCI slots

Figure 5 M440LX Server Baseboard Clock Distribution

Interrupts and I/O APIC

The M440LX interrupt architecture accommodates both PC-compatible 8259 PIC modes and dual-processor APIC mode interrupts.  In addition, interrupt steering is required for offloading of PCI interrupts to the i960 RD and control of rerouting to ISA IRQs.  Special logic is required to implement this custom interrupt scheme. The M440LX Interrupt Steering and Server Management Interface Controller (MISSMIC) provides this.

For PC-compatible mode, the Intel PIIX4 provides two 82C59-compatible interrupt controllers.  The two embedded interrupt controllers are cascaded with interrupt levels 8-15 entering on the second level of the primary interrupt controller (per normal PC/AT compatibility).  A single interrupt signal is presented to the processors, to which only one processor will respond.

For APIC mode, M440LX baseboard interrupt architecture incorporates the Intel I/O APIC device to manage and broadcast interrupts to local APICs in each processor.  The I/O APIC monitors interrupt requests from devices. On occurrence of an interrupt the I/O APIC sends a message corresponding to the interrupt across a three wire serial interface to the local APICs.  The APIC bus minimizes interrupt latency time for compatibility interrupt sources, in both single and dual processor operation in Windows NT, Novell NetWare, and the leading UNIX operating systems.

The entire baseboard APIC structure consists of a single I/O APIC device with 24 input interrupt requests. The I/O APIC also manages the 16 PC/AT compatibility interrupts and also manages the 8 interrupt levels associated with PCI interrupts on the Primary and Secondary PCI bus segments. This supports more efficient interrupt processing and offloads the polling of interrupts from devices beneath the i960 RD bridge by the host processor.

The i960 RD manages interrupts from PCI devices beneath it and services the interrupt locally, with the I/O APIC providing interrupt notification to the host processor. This allows the i960 RD to lend intelligence to handling of interrupts from add-in cards and embedded SCSI devices, by intercepting the interrupt and servicing it locally.  This I2O interrupt steering logic is under program control using a 5-bit control register in the i960 RD, that determines the mapping of PCI interrupts from each device and slot.  The interrupts are then logically ORed in the MISSMIC as 4 interrupts to the i960 RD or I/O APIC.  The i960 RD can also generate an interrupt on PCI-P using the “door bell” messaging mechanism.

Table 4 M440LX Interrupt StructureInterrupt Routing

The following table describes the interrupt routing of the Primary PCI bus segment interrupts.  Interrupts shared between slots are cascaded to avoid conflicts, since most PCI cards use P_INTA as their external interrupt connection.

| PCI-P INT | I/O APIC Interrupt | PCI-P slot P0 | PCI-P slot P1 | 8-bit SCSI | PCI-P slot P2 | Cirrus SVGA | Intel i960 RD | Intel PIIX4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| P_INTA | 16 | A | D | - | B | - | C | pull-up |
| P_INTB | 17 | B | A | - | C | - | D | pull-up |
| P_INTC | 18 | C | B | A | D | - | A | pull-up |
| P_INTD | 19 | D | C | - | A | - | B | C |

Table 5 PCI-P Interrupt Routing

The following table describes the interrupt routing of the Secondary PCI bus segment interrupts.  Even though each interrupt has an input pin to the MISSMIC (for I2O purposes), interrupts are cascaded between PCI-S slots to simplify logic in the MISSMIC when directing them to I/O APIC inputs.

| PCI-S INT | I/O APIC Interrupt | PCI-S slot S0 | PCI-S slot S1 | PCI-S slot S2 | PCI-S slot S3 | Symbios SCSI-A | Symbios SCSI-B | Intel i960 RD_INT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| S_INTA | 20 | D | C | B | D | A | A | RD_INTA |
| S_INTB | 21 | A | D | C | A | - | - | RD_INTB |
| S_INTC | 22 | B | A | D | B | - | - | RD_INTC |
| S_INTD | 23 | C | B | A | C | - | - | RD_INTD |

Table 6 PCI-S Interrupt Routing

PCI Interrupt Rerouting

Some MP operating systems are Currently unable to handle interrupts from PCI slots and devices as pure PCI interrupts, via inputs 16-19 (Primary PCI bus) or 20-23 (Secondary PCI bus) of the I/O APIC.  These MP network operating systems expect PCI interrupts to be delivered as ISA IRQs.  MP operating systems may also expect some interrupts from the PC-compatible PIC in the PIIX4, and others from the I/O APIC (Mixed Mode).  Some device drivers check whether the device uses one of the traditional IRQs, and if not (when the PCI interrupt is connected directly to the I/O APIC), the drivers may fails to install or run properly.  The PIIX4 performs internal PCI to IRQ interrupt steering so PCI interrupts can be delivered to the PIC.  However, the PCI interrupt steering feature is unidirectional, which means that it cannot redirect PCI interrupts to the I/O APIC.

For these reasons, the MISSMIC incorporates an external PCI to IRQ rerouter circuit, that can be programmed to pass PCI interrupts through to inputs 16-19 and 20-23 of the I/O APIC, or deliver a specific PCI interrupt to an IRQ.  Using the SCU, a PCI interrupt can be individually rerouted to one of these IRQ lines: IRQ3, IRQ4, IRQ5, IRQ6, IRQ7, IRQ9, IRQ10, IRQ11, IRQ12, IRQ14, or IRQ15.

Interrupt Sources

The interrupt map is defined using configuration registers in the PIIX4 and the I/O controller.  I/O Redirection Registers in the I/O APIC are provided for each interrupt signal, which define hardware interrupt signal characteristics for APIC messages sent to local APIC(s).

| Interrupt | I/O APIC level | Description |
| --- | --- | --- |
| INTR | INT0 | Processor interrupt |
| NMI |  | NMI from MISSMIC to processor |
| IRQ1 | INT1 | Keyboard interrupt |
| Cascade | INT2 | Interrupt signal from second 8259 in PIIX4 |
| IRQ3 | INT3 | Serial port A or B interrupt from 87307VUL device, user-configurable. |
| IRQ4 | INT4 | Serial port A or B interrupt from 87307VUL device, user-configurable. |
| IRQ5 | INT5 | Parallel port - LPT2 |
| IRQ6 | INT6 | Floppy disk |
| IRQ7 | INT7 | Parallel port - LPT1 |
| IRQ8_L | INT8 | RTC interrupt |
| IRQ9 | INT9 | Open |
| IRQ10 | INT10 | Open |
| IRQ11 | INT11 | Open |
| IRQ12 | INT12 | Mouse interrupt |
|  | INT13 | Reserved |
| IRQ14 | INT14 | Compatibility IDE interrupt from primary channel IDE devices 0 and 1 |
| IRQ15 | INT15 | Open |
| P_INTA_L | INT16 | PCI-P Interrupt signal A |
| P_INTB_L | INT17 | PCI-P Interrupt signal B |
| P_INTC_L | INT18 | PCI-P Interrupt signal C |
| P_INTD_L | INT19 | PCI-P Interrupt signal D |
| S_INTA_L | INT20 | PCI-S Interrupt signal A |
| S_INTB_L | INT21 | PCI-S Interrupt signal B |
| S_INTC | INT22 | PCI-S Interrupt signal C |
| S_INTD_L | INT23 | PCI-S Interrupt signal D |
| SMI_L |  | System Management Interrupt. General-purpose error indicator from a control PAL that provides an SMI_L from non-traditional error sources (PERR_L, SERR_L, and others). |

Table 7 Interrupt Definitions

Baseboard Jumper Settings

A single 15-pin inline headers provide a total of four 3-pin jumper blocks that control various configuration options, as shown in the figure below.  The shaded areas show default jumper placement for each configurable option.

Table 8 Configuration Jumpers

| Option | Description |
| --- | --- |
| CMOS Clear | If pins 1 and 2 of J26 are jumpered (default), NVRAM contents are preserved through system reset. If pins 2 and 3 of J26 are jumpered, NVRAM contents are set to manufacturing default during system reset. |
| Password Clear | If pins 5 and 6 of J26 are jumpered (default), the current system password is maintained during system reset. If pins 6 and 7 of J26 are jumpered, the password is cleared on reset. |
| Recovery or Normal BIOS boot block | If pins 9 and 10 of J26 are jumpered (default), address A16 is inverted so system BIOS does not reside at the top of flash, where the write-protected Recovery BIOS region is located. If the system BIOS gets corrupted (i.e. Power outage durring BIOS update), and you are unable to reload a fresh copy from the floppy disk, then install the jumper between pins 10 and 11 of J26, which causes A16 to become non-inverted and enables the system to boot from the Recovery BIOS. |
| Boot Block Write Protect | If pins 13 and 14 of J26 are jumpered (default), the BIOS boot block is write-protected. If pins 14 and 15 of J26 are jumpered, the boot block is erasable and programmable. WARNING: Incorrect programming of the boot block will render the system unbootable. |

Table 9 Configuration Jumper Options

1.4	EDO Memory Module

EDO DRAM Array

The memory array on the module consists of eight 72-bitDIMM sockets.  These allow for up to 1GB of DRAM when using 128MB 3.3V JEDEC standard parallel detect DIMMs.  ECC bits support the detection and correction of single bit and detection of double bit errors by the memory controller in the Intel 82440LX PAC. The memory controller in the 82440LX PAC set can automatically detect and initialize the memory array, depending upon the type, size, and speed of installed DIMM devices.  8, 16, 32, 64, and 128 MB DIMMs are supported.  A list of tested DIMMs is available to you through your Intel representative.

Currently, even though 1GB total memory is possible, the Pentium II processor module can only cache 512MB.  Therefore it is only necessary to populate the memory module with up to 512MB for maximum system performance. Loading the memory module with 8 (50/60 ns) EDO DIMMs gives a timing profile of x-3-3-3 for a burst read and x-3-3-3  for a burst write while a loading of 4 DIMMs can provide a x-2-2-2 profile. Note that faster timing is available when only 4 DIMMs are installed.

Figure 6 Memory Module Layout

Memory is partitioned as 8 banks of DRAM, 1 bank per installed DIMM.  The chip set provides a row address strobe (RCSAn_L) for each bank, plus a copy of each (RCSBn_L) to evenly distribute the loading incurred by the DIMM array, resulting in improved signal quality.  Column address strobes (CDQAx_L) for all data bits are also provided.  DIMM sockets should be populated in sequence, i.e. DIMM-0, then DIMM-1, and so on with DIMM-7 last.  If 4 DIMMs are used rather than 8, faster timing is available (refer to “Timing Specifications” later in this chapter).  The following diagram shows the correspondence between installed DIMMs, RCSAn_L/RCSBn_L signals, and DRAM row boundary (DRB) values.

Figure 7 M440LX EDO Memory module  Block Diagram

The M440LX EDO memory module provides clock generation onboard, in anticipation of a follow-on SDRAM version of the board.  Each SDRAM DIMM requires 4 clock inputs, so placing clock generation on the memory module obviates the need to run multiple clocks through the connector interface.

The Baseboard Management Controller (BMC) can access server management information, stored locally on the memory module, through the I2C interface.  This information includes the board type, serial number, number of installed DIMMs, and their speed.  This interface is also used to control testability features, such as the disabling of individual DIMMs or controlling of clock generation.

A 242-pin “Slot 1”-style edge connector on the module provides connection of address, data, ECC, control, I2C, power, clocks, and other signals between memory and the baseboard.  The main body of this connector interface is based on signals provided by the 82440LX PAC.  It is compatible with the SDRAM version of the module, since the chip set supports both EDO and SDRAM devices.

1.5	RPX Module

The RPX module is an option for the M440LX DP Server Baseboard.  With the RPX module installed you gain the ability to use I2O on the secondary PCI bus including I2O RAID through the integrated Symbios SYM53C875 Ultra SCSI controllers.

For more information on I2O see http://developer.intel.com/design/IIO/

Figure 8 RPX Module Diagram

The RPX module DRAM subsystem consists of two x36 SIMM sockets providing one or two banks of interleaved DRAM.  The data path and memory is protected with byte wide parity.  The interleaved DRAM subsystem supports burst memory reads with a 2-0-0-0 wait state profile, and burst memory writes with a 1-0-0-0 wait state profile using 60 ns memory devices. 70 ns and 50 ns  SIMM devices are not supported on the RPX module.

The RPX module will support a single, byte wide, bank of non-volatile SRAM (NVRAM).  This memory can be written on a byte wide basis, compared to flash memory, which can also be written to, but only on a block basis.  The NVRAM will reside in the memory space controlled by the bank 1 memory controller on the 80960RD.  The plan of record is to provide 8 KB of NVRAM, but the board design will support 8 KB or 32 KB of NVRAM.  The size of NVRAM required would have to be determined prior to manufacturing the board -- it is not a field upgrade option.

Server management logic is included on the RPX module to provide inventory management information and to monitor battery temperature.  The server management information is accessible by the baseboard through the I2C interface.

Battery Backup

The RPX module contains circuitry to provide battery backup of the DRAM SIMMs in the event of a system power failure.  This allows critical data (such as write-back disk cache data) to be preserved in the event of a power failure.  The battery is mounted on the upper portion of the RPX module.

Figure 9 Battery Backup Block Diagram

The cache dirty and charger enable signals from the write port is used to control the battery circuitry.  If there is dirty data in the cache (CDIRTY# asserted) when the power fail detector senses system power (VCC) dropping, it will switch the source of VBB from VCC to the battery.  If there is not dirty data in the cache, VBB will drop when VCC drops.  The battery is physically a 2.4 V device, so a DC-to-DC converter is required to step this voltage up to 5 V.  In addition to the battery charging and switching circuitry, the battery backup block also includes circuitry to generate the DRAM refresh.  This circuitry is activated when a power failure has occurred, and generates CAS# before RAS# refresh cycles.

The battery charger can be enabled or disabled via the charger enable bit in the write port.  The status of the battery can be read through the read port to detect battery presence/absence and charge state: charge pending, charge in progress, or charge complete.

Note:  The battery must be disconnected prior to removing and servicing the RPX module.  Disconnecting the battery prevents potentially installing or removing a SIMM that has power applied to it.

2.	Server Management

The M440LX baseboard server management features are implemented using two separate microcontrollers and one ASIC:

·	Baseboard Management Controller (BMC)

·	Front Panel Controller (FPC)

·	Madrona Interrupt Steering and Server Management Interface Chip (MISSMIC)

The management controllers are specially programmed microcontrollers that monitor various server management functions, and communicate their management information on an internal I2C-based “Intelligent Management Bus”. The Intelligent Management Bus extends throughout the baseboard, processor board, and system chassis.  The BMC can also be accessed from the ISA bus via the MISSMIC ASIC.

In addition to the management controllers implemented on the baseboard and processor board, the chassis may implement additional management controllers that connect to the Intelligent Management Bus. For example, the Balboa-II chassis implements:

·	Power Share Controller (PSC)

·	Hot-swap Controller (HSC)

The following diagram illustrates M440LX server management architecture.  A brief description of the hardware architecture follows

Figure 10 M440LX Server Management Architecture

2.1	Baseboard Management Controller (BMC)

The BMC is an 8051-compatible microcontroller located on the M440LX baseboard.  The BMC directly monitors baseboard power supply and SCSI termination voltages using an separate onboard Analog to Digital Converter (ADC), and checks the status of the fan failure indicators on the baseboard.  The BMC also monitors system temperature sensors.

If enabled, the BMC will generate an internal Event Message when any monitored parameter is outside defined thresholds.  This triggers the BMC’s System Event Logging function, causing it to store the event in the System Event Log. The BMC acts as the primary communications gateway between ‘ISA’ and the Intelligent Management Bus. System Management Software and BIOS goes through the BMC to communicate with other controllers and devices on the IMB, such as the FPC.

The BMC monitors processor power supply voltage levels, provides access to DIMM configuration and presence information, monitors processor thermal trip and internal error signals, and manages two I2C thermal sensors; one for each processor.  Fault Resilient Booting (FRB) Level 3 is also managed by the BMC, which controls the ability to boot using either processor in the event of a catastrophic processor failure.

A Serial I2C EEPROM associated with the secondary baseboard temperature sensor also contains an EEPROM that is used by the Front Panel Controller (FPC) to retain system power state during power off conditions. Thus, the FPC and BMC must share access to that device.

The BMC incorporates several server management features related to the processor subsystem:

·	Processor near-heatsink temperature measurement

·	Processor internal overtemperature output signal monitoring

·	Processor error signal output monitoring

·	VRM set point and output voltage monitoring

·	CPU subsystem 1.5V and 2.5V voltage regulator output monitoring

·	Facilities for fault-resilient booting

These signals and sensors are accessible by the Baseboard Management Controller (BMC).

Fault Resilient Booting

The BMC implements Fault Resilient Booting (FRB) levels 1, 2, and 3.  If two processors are installed and the processor designated as the bootstrap processor fails to complete the boot process, FRB attempts to boot the system using the alternate processor.

·	FRB level 1 is for recovery from a BIST failure detected during POST.  This FRB recovery is fully handled by BIOS code.

·	FRB level 2 is for recovery from a Watchdog timeout during POST.  The Watchdog timer for FRB level 2 detection is implemented in the BMC.

·	FRB level 3 is for recovery from a Watchdog timeout on Hard Reset / Power-up.  Hardware functionality for this level of FRB is provided by the BMC on the processor subsystem.

FRB-3 is managed by the BMC, which controls the ability to boot using either processor in the event of a catastrophic processor failure.  On power up, a timer starts that can only be stopped by a healthy processor using the GPIO bit, FRB_TMRHLT_L, on the Super I/O chip.  If processor 0 fails to halt the FRB timer before timeout, the controller asserts STOP_FLUSH to the processor and asserts FRB_RST_L for 10ms.  When the system comes out of reset, processor 0 is unable to act as the boot processor allowing the other processor to take over the boot process.

2.2	Front Panel Controller (FPC)

The FPC, located on the baseboard, manages system power on/off control, system reset, and front panel NMI buttons, along with an external I2C interface.  The device is powered from the +5V standby power supply, to stay alive when system power is switched off.  The FPC controls main power to the baseboard and processor board, and is responsible for monitoring all sources of power control both on and off the baseboard including the Front Panel, Server Monitor Module, PIIX4, and RTC power control signals.  The FPC also detects chassis intrusion, by monitoring an external switch.

2.3	I2C Isolation Buffers and Auxiliary I2C Connector

Buffers are provided to isolate the baseboard temperature sensors, auxiliary I2C connector, and FPC from the rest of the I2C bus.  These buffers, running on the standby supply, keep the bus alive to the FPC even though main power is switched off.  This allows the FPC to communicate with its I2C EEPROM (in the secondary baseboard temperature sensor) at all times, and provides a way to remotely control power via the auxiliary I2C connector. A shorted I2C connection at the auxiliary I2C connector will prevent restoration of main power.

2.4	Madrona Interrupt Steering and Server Management Interface Chip (MISSMIC)

Communication between the two microcontrollers on the baseboard is done using the I2C bus.  Communication between this distributed controller network, SMI handler, and Systems Management Software (SMS) running on the server, is done using the BMC and MISSMIC.  The MISSMIC functions as a bridge between the BMC and ISA bus.  The MISSMIC also gates and redirects SMI_L and NMI, generating SERR_L, and performs PCI to IRQ rerouting.  The MISSMIC also provides a mailbox register interface designed to work with SMS and SMI_L handler code across the ISA interface.

2.5	System Fan Interface

The M440LX server baseboard provides several 3-pin, shrouded, and keyed fan connectors.  Two of these connectors, located next to each Pentium II processor socket on the processor board, is for a standard fansink, with +5V and GND only.  The remaining connectors on the baseboard attach to a fan equipped with a sensor that indicates whether the fan is operating (tachometer fan).  The sensor pins for these fans are routed to the BMC for failure monitoring.  Each connector has the following pinout:

| Pin | Signal |
| --- | --- |
| 1 | +12V |
| 2 | Fan Fail Sensor |
| 3 | GND |

Table 10 Tachometer Fan Connector Pinout

The fansink connector has the following pinout:

| Pin | Signal |
| --- | --- |
| 1 | +5V |
| 2 | no connect |
| 3 | GND |

Table 11 Fansink Connector Pinout

3.	Memory and Other Resource Mappings

3.1	Extended Memory

Extended memory on M440LX is defined as all address space greater than 1 MB.  The Extended Memory region covers 4 GB of address space from addresses 0100000h to FFFFFFFFh, as shown in the following figure.

Figure 11 Extended Memory Map

3.2

I/O Map

The 82440LX PAC allows I/O addresses to be mapped to the processor bus or through designated bridges in a multi-bridge system.  Other PCI devices, including the PCI-to-PCI Bridge and PIIX4 have built-in features that support PC-compatible I/O devices and functions, which are mapped to specific addresses in I/O space.  On the M440LX baseboard, the PIIX4 provides the bridge to ISA functions, which must be disabled in the PCI-to-PCI bridge.

The I/O map in the following table shows the location in M440LX I/O space of all directly I/O-accessible registers.  PCI configuration space registers for each device control mapping in I/O and memory spaces, and other features that may affect the global I/O map. The Super I/O chip contains configuration registers that are accessed through an index and data port mechanism

Table 12 M440LX I/O Map

| Address(es) | Resource | Device | Notes |
| --- | --- | --- | --- |
| 0000h - 000Fh | DMA Controller 1 | PIIX4 |  |
| 0010h - 001Fh | DMA Controller 1 | PIIX4 | aliased from 0000h - 000Fh |
| 0020h - 0021h | Interrupt Controller 1 | PIIX4 |  |
| 0022h - 0023h |  |  |  |
| 0024h - 0025h | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 0026h - 0027h |  |  |  |
| 0028h - 0029h | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 002Ah - 002Bh |  |  |  |
| 002Ch - 002Dh | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 002Eh - 002Fh | Super I/O Index and Data Ports | 87307 |  |
| 0030h - 0031h | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 0032h - 0033h |  |  |  |
| 0034h - 0035h | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 0036h - 0037h |  |  |  |
| 0038h - 0039h | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 003Ah - 003Bh |  |  |  |
| 003Ch - 003Dh | Interrupt Controller 1 | PIIX4 | aliased from 0020h - 0021h |
| 003Eh - 003Fh |  |  |  |
| 0040h - 0043h | Programmable Timers | PIIX4 |  |
| 0044h - 004Fh |  |  |  |
| 0050h - 0053h | Programmable Timers | PIIX4 | aliased from 0040h - 0043h |
| 0054h - 005Fh |  |  |  |
| 0060h | Keyboard Controller | 87307 |  |
| 0061h | NMI Status & Control Register | PIIX4 |  |
| 0062h |  |  |  |
| 0063h | NMI Status & Control Register | PIIX4 | aliased |
| 0064h | Keyboard Controller | 87307 |  |
| 0065h | NMI Status & Control Register | PIIX4 | aliased |
| 0066h |  |  |  |
| 0067h | NMI Status & Control Register | PIIX4 | aliased |
| 0068h-006Fh |  |  |  |
| 0070h | NMI Mask (bit 7) & RTC Address (bits 6::0) | PIIX4 |  |
| 0071h | RTC Data | PIIX4 |  |
| 0072h | RTC Extended Index | PIIX4 |  |

| 0073h | RTC Extended Data | PIIX4 |  |
| --- | --- | --- | --- |
| 0074h | NMI Mask (bit 7) & RTC Address (bits 6::0) | PIIX4 | aliased from 0070h |
| 0075h | RTC Data | PIIX4 | aliased from 0071h |
| 0076h-007Fh |  |  |  |
| 00A0h - 00A1h | Interrupt Controller 2 | PIIX4 |  |
| 00A2h- 00A3h |  |  |  |
| 00A4h - 00A15 | Interrupt Controller 2) | PIIX4 | aliased from 00A0h - 00A1h |
| 00A6h 00A7h |  |  |  |
| 00A8h - 00A19 | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00AAh 00ABh |  |  |  |
| 00ACh - 00ADh | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00AEh 00AFh |  |  |  |
| 00B0h - 00B1h | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00B2h | Advanced Power Management Control | PIIX4 |  |
| 00B3h | Advanced Power Management Status | PIIX4 |  |
| 00B4h - 00B5h | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00B6h 00B7h |  |  |  |
| 00B8h - 00B9h | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00BAh - 00BBh |  |  |  |
| 00BCh - 00BDh | Interrupt Controller 2 | PIIX4 | aliased from 00A0h - 00A1h |
| 00BEh- 00BFh |  |  |  |
| 00C0h | DMA2 CH0 Base and current address | PIIX4 |  |
| 00C1h | DMA2 CH0 Base and current address | PIIX4 | aliased from 00C0h |
| 00C2h | DMA2 CH0 Base and current count | PIIX4 |  |
| 00C3h | DMA2 CH0 Base and current count | PIIX4 | aliased from 00C2h |
| 00C4h | DMA2 CH1 Base and current address | PIIX4 |  |
| 00C5h | DMA2 CH1 Base and current address | PIIX4 | aliased from 00C4h |
| 00C6h | DMA2 CH1 Base and current count | PIIX4 |  |
| 00C7h | DMA2 CH1 Base and current count | PIIX4 | aliased from 00C6h |
| 00C8h | DMA2 CH2 Base and current address | PIIX4 |  |
| 00CAh | DMA2 CH2 Base and current address | PIIX4 | aliased from 00C8h |
| 00CAh | DMA2 CH2 Base and current count | PIIX4 |  |
| 00CBh | DMA2 CH2 Base and current count | PIIX4 | aliased from 00CAh |
| 00CCh | DMA2 CH3 Base and current address | PIIX4 |  |
| 00CDh | DMA2 CH3 Base and current address | PIIX4 | aliased from 00CCh |
| 00CEh | DMA2 CH3 Base and current count | PIIX4 |  |
| 00CFh | DMA2 CH3 Base and current count | PIIX4 | aliased from 00CEh |
| 00D0h | DMA2 Status(r) Command(w) | PIIX4 |  |
| 00D1h | DMA2 Status(r) Command(w) | PIIX4 | aliased from 00D0h |
| 00D2h | DMA2 Request | PIIX4 |  |
| 00D3h | DMA2 Request | PIIX4 | aliased from 00D2h |
| 00D4h | DMA2 Write single mastk bit | PIIX4 |  |
| 00D5h | DMA2 Write single mastk bit | PIIX4 | aliased from 00D4h |
| 00D6h | DMA2 Channel mode | PIIX4 |  |
| 00D7h | DMA2 Channel mode | PIIX4 | aliased from 00D6h |
| 00D8h | DMA2 clear byte pointer | PIIX4 |  |
| 00D9h | DMA2 clear byte pointer | PIIX4 | aliased from 00D8h |
| 00DAh | DMA2 Master clear | PIIX4 |  |
| 00DBh | DMA2 Master clear | PIIX4 | aliased from 00DAh |
| 00DCh | DMA2 Clear mask | PIIX4 |  |
| 00DDh | DMA2 Clear mask | PIIX4 | aliased from 00DCh |
| 00DEh | DMA2 Read/write all mask register bits | PIIX4 |  |
| 00DFh | DMA2 Read/write all mask register bits | PIIX4 | aliased from 00DEh |
| 00F0h | Clear coprocessor error | PIIX4 | Resets IRQ13 |
| 03F0h - 03F7h | Floppy Disk Controller | 87307 |  |
| 0370h - 0375h | Secondary Floppy |  |  |
| 0376h | Secondary IDE |  |  |
| 0377h | Secondary IDE/Floppy |  |  |
| 04D0h | Interrupt Controller 1 Edge/Level control | PIIX4 |  |
| 04D1h | Interrupt Controller 2 Edge/Level control | PIIX4 |  |
| 0CA0h | Secondary PCI Interrupt Routing | MISSMIC |  |
| 0CA1h | MISSMIC Data Register | MISSMIC | Server management mailbox |
| 0CA2h | MISSMIC Control/Status Register | MISSMIC | registers. |
| 0CA3h | MISSMIC Flags Register | MISSMIC |  |
| 0CA4h-0CA7h | PCI to IRQ Interrupt Routing | MISSMIC |  |
| 0CF9h | Reset control | PIIX4 |  |
| 0220h - 022Fh | Serial Port A |  |  |
| 0238h - 023Fh | Serial Port B |  |  |
| 02E8h - 02EFh | Serial Port B |  |  |
| 02F8h - 02FFh | Serial Port B |  |  |
| 0338h - 033Fh | Serial Port B |  |  |
| 03E8h - 03EFh | Serial Port A |  |  |
| 03F8h - 03FFh | Serial Port A (Primary) |  |  |
| 0278h - 027Fh | Parallel Port 3 |  |  |
| 0378h - 037Fh | Parallel Port 2 | 87307 |  |
| 03BCh - 03BFh | Parallel Port 1 (Primary) | 87307 |  |
| 0678h - 067Ah | Parallel Port (ECP) | 87307 |  |
| 0778h - 077Ah | Parallel Port (ECP) | 87307 |  |
| 07BCh - 07BEh | Parallel Port (ECP) | 87307 |  |
| 0080h - 0081h | BIOS Timer |  |  |
| 0080h - 008Fh | DMA Low Page Register |  | PIIX4 |
| 0090h - 0091h | DMA Low Page Register (aliased) |  | PIIX4 |
| 0092h | System Control Port A ( PC-AT control Port) (this port not aliased in DMA range) |  | PIIX4 |
| 0093h - 009Fh | DMA Low Page Register (aliased) |  | PIIX4 |
| 0094h | Video Display Controller |  |  |
| 00F8h - 00FFh | x87 Numeric Coprocessor |  |  |
| 0102h | Video Display Controller |  |  |
| 0170h - 0177h | Secondary Fixed Disk Controller (IDE) |  | PIIX4 (not used) |
| 01F0h - 01F7h | Primary Fixed Disk Controller (IDE) |  | PIIX4 |
| 0200h - 0207h | Game I/O Port |  | Not used |
| 03B4h - 03BAh | Monochrome Display Port |  |  |
| 03C0h - 03CFh | Video Display Controller |  |  |
| 03D4h - 03DAh | Color Graphics Controller |  |  |
| 0400h - 043Fh | DMA Controller 1, Extended Mode Registers. |  | PIIX4 |
| 0461h | Extended NMI / Reset Control |  | PIIX4 |
| 0462h | Software NMI |  | PIIX4 |
| 0480h - 048Fh | DMA High Page Register. |  | PIIX4 |
| 04C0h - 04CFh | DMA Controller 2, High Base Register. |  |  |
| 04D4h - 04D7h | DMA Controller 2, Extended Mode Register. |  |  |
| 04D8h - 04DFh | Reserved |  |  |
| 04E0h - 04FFh | DMA Channel Stop Registers |  |  |
| 0800h - 08FFh | NVRAM |  |  |
| 0C80h - 0C83h | EISA System Identifier Registers |  | PIIX4 |
| 0C84h | Board Revision Register |  |  |
| 0C85h - 0C86h | BIOS Function Control |  |  |
| 0CF8h | PCI CONFIG_ADDRESS Register |  | Located in PAC |
| 0CFCh | PCI CONFIG_DATA Register |  | Located in PAC |
| 46E8h | Video Display Controller |  |  |
| xx00 - xx1F* | SCSI registers |  | Refer to SCSI chip doc. |

*SCSI I/O base address is set using configuration registers.

3.3

Device Number and IDSEL Mapping

|  | Primary PCI Bus | Secondary PCI Bus |
| --- | --- | --- |
| IDSEL | Device # | Device | Device # | Device |
| 31 | 10100b | PIIX4 | 01111b |  |
| 30 | 10011b | i960® RP PCI-to-PCI bridge | 01110b |  |
| 29 | 10010b |  | 01101b |  |
| 28 | 10001b | CL-GD54M40 video chip | 01100b |  |
| 27 | 10000b | PCI-P Slot 2 | 01011b |  |
| 26 | 01111b | Symbios SYM53C810 | 01010b |  |
| 25 | 01110b | PCI-P Slot 1 | 01001b |  |
| 24 | 01101b | PCI-P Slot 0 | 01000b |  |
| 23 | 01100b |  | 00111b |  |
| 22 | 01011b |  | 00110b |  |
| 21 | 01010b |  | 00101b | PCI-S Slot 3 |
| 20 | 01001b |  | 00100b | Wide SCSI B (SYM53C875) |
| 19 | 01000b |  | 00011b | PCI-S Slot 2 |
| 18 | 00111b |  | 00010b | PCI-S Slot 1 |
| 17 | 00110b |  | 00001b | PCI-S Slot 0 |
| 16 | 00101b |  | 00000b | Wide SCSI A (SYM53C875) |
| 15 | 00100b |  | N/A |  |
| 14 | 00011b |  | N/A |  |
| 13 | 00010b |  | N/A |  |
| 12 | 00001b |  | N/A |  |
| 11 | 00000b | Hardwired to host bridge | N/A |  |

Table 13 PCI Configuration IDs and Device Numbers

4.	BIOS, Setup, SCU and SCSI Utility

4.1	BIOS Overview

The term “BIOS" refers to the following:

·	System BIOS, that controls basic system functionality using stored configuration values.

·	Configuration Utilities (CU) consisting of Flash ROM-resident Setup utility and system memory-resident System Configuration Utility (SCU), that provides user control of configuration values stored in NVRAM and battery-backed CMOS configuration RAM.

·	Flash Memory Update utility (IFLASH), that loads predefined areas of Flash ROM with Setup, BIOS, and other code/data.

The following figure shows the relationship between BIOS components and register spaces. Unshaded areas are loaded into Flash using the Flash Memory Update Utility (IFLASH).

Figure 12 M440LX BIOS Architecture

4.2	System BIOS

The system BIOS is the core of the Flash ROM-resident portion of the BIOS. The system BIOS provides standard PC-BIOS services and some new industry standards, such as Plug and Play, DMI. In addition, the system BIOS provides support for these M440LX-specific features: security features, multiple-speed processor support, SMP support, fault resilient booting (FRB), logging of critical events, server management features, CMOS configuration RAM defaults, multiple language support, defective DIMM detection and remapping, automatic detection of video adapters, PCI BIOS interface, option ROM shadowing, system information reporting, ECC support, SMI support, user-supplied BIOS support, L2 cache support, I2O support, memory sizing, boot drive sequencing, and resource allocation support.

The BIOS Setup and System Configuration Utility (SCU) are covered in detail in the M440LX Product Guide.

1.

5.	Boardset Specifications

This chapter specifies the operational parameters and physical characteristics for M440LX.  This is a board-level specification only.  System specifications are beyond the scope of this document.

5.1	Absolute Maximum Ratings

Operation of M440LX at conditions beyond those shown in the following table may cause permanent damage to the system (provided for stress testing only).  Exposure to absolute maximum rating conditions for extended periods may affect system reliability.

| Operating Temperature | 0°C to +55°C * |
| --- | --- |
| Storage Temperature | -55°C to +150°C |
| Voltage on any signal with respect to ground | -0.3V to VDD + 0.3V ** |
| 3.3V Supply Voltage with Respect to ground | -0.3 to +3.63V |
| 5V Supply Voltage with Respect to ground | -0.3 to +5.5V |

* Chassis design must provide proper airflow to avoid exceeding Pentium Pro maximum case temperature.
	** VDD means supply voltage for the device.

Table 14 Absolute Maximum Ratings

Further topics in this chapter specify normal operating conditions for M440LX.

5.2	Electrical Specifications

DC specifications for M440LX power connectors and module power budgets, are summarized here.  Electrical characteristics for major connector interfaces (including DC and AC specifications), can be obtained from other documents:

·	PCI Connectors -- PCI Local Bus Specification Rev. 2.1

·	ISA slots -- EISA Bus Specification

Power Connection

Main power supply connection is obtained using the 24-pin main connector, which attaches to the power supply via 18 AWG wire of the color shown below.

Table 0-1.  24-pin Main Power Connector Pinout

| Pin | Signal | Color | Pin | Signal | Color |
| --- | --- | --- | --- | --- | --- |
| 1 | +5 Vdc | Red | 13 | +5 Vdc | Red |
| 2 | +5 Vdc | Red | 14 | +5 Vdc | Red |
| 3 | -5 Vdc | White | 15 | +5 Vdc | Red |
| 4 | -12Vdc | Blue | 16 | +5 Vdc | Red |
| 5 | COM | Black | 17 | COM | Black |
| 6 | COM | Black | 18 | COM | Black |
| 7 | COM | Black | 19 | COM | Black |
| 8 | COM | Black | 20 | COM | Black |
| 9 | COM | Black | 21 | COM | Black |
| 10 | +3.3 Vdc | Orange | 22 | +3.3 Vdc | Orange |
| 11 | +12 Vdc | Yellow | 23 | +3.3 Vdc | Orange |
| 12 | +12 Vdc | Yellow | 24 | +12 Vdc | Yellow |