Board Name:	M4P

Part #:		09-00190-xx

Size:			Baby AT (8 1/2” x 13”)			Chip Sets:		Intel 82420 PCI set

SMC 665 Super I/O

Expansion Slots:		5 16-bit ISA				Cache Options:		128K/ 256K (32K x 8 SRAM)

2 32-bit 120-pin PCI

1 shared PCI ISA				BIOS: 			Phoenix BIOS on 1MB flash BIOS

Auto detection of memory size

Processor Specifications:	486SX25; SX33, PQFP

486DX33, PGA				IDE Interface:		Resident 40-pin IDE connectors

486DX2/50; 486DX2/66, PGA

Floppy Support:		360K, 1.2MB, 1.44MB or 2.88MB

Upgrade CPU:		P24T; 238-pin ZIP socket			Communication Ports:	2 on-board 16550 serial ports

1 on-board bi-directional port

Memory:		(4) 72-pin SIMM sockets to accommodate:

Keyboard:		Standard AT-Style DIN connector			 	1MB x 36 (4MB); 2MB x 36 (8MB)

4MB x 36 (16MB); 8MB x 36 (32MB)

MAX: 128MB

Cache Size Selection

| Jumper | Configuration | Setting |
| --- | --- | --- |
| J52 |

256K L2 Cache

128 L2 Cache

Pins 2-3

Pins 1-2

J53

256K L2 Cache

128 L2 Cache

Pins 1-2

Pins 2-3

J58

256K L2 Cache

128 L2 Cache

Installed

Not Installed

J61

L2 Cache in WT mode

L2 Cache in WB mode

Pins 1-2

Pins 2-3

On-Board I/O Connectors

| Jumper | Configuration | Setting |
| --- | --- | --- |
| J14 | PCI #3 (Slave, Shared with ISA Slot J6) |
|  | J15 | PCI #2 (Master/ Slave) |
|  | J17 | PCI #1 (Master/ Slave) |
|  | J27 |

PCI IRQ 5

IRQ5 Available for ISA

Installed

Not Installed

J28

PCI IRQ 11

IRQ11 Available for ISA

Installed

Not Installed

J29

PCI IRQ 15

IRQ15 Available for ISA

Installed

Not Installed

CPU Selection

| Jumper | Configuration | Setting |
| --- | --- | --- |
| J40 |

33Mhz

25Mhz

Installed

Not Installed

J59

487/P23T/486

P24T

Installed

Not Installed

J60

P24T in WB mode

P24T in WT mode

Installed

Not Installed

J65

P24D

All Other CPUs

Installed

Not Installed

J66

P24D

All Other CPUs

Installed

Not Installed

J67

P24C (2x Clock)

P24t, P24CT, 487SX, 486SX, P23S, 486DX486DX2, P24C (3x Clock), P24S, and P24S

Installed

Not Installed

J68

P24D

All Other CPUs

Installed

Not Installed

J69

P24T, P24CT, P23S, P24C, P4S, P24S, and P24D

487SX, 486SX, 486DX, and 486DX2

Installed

Not Installed

J71

486SX

All Other CPUs

Pins 2-3

Pins 1-2, 3-4

J72

P24D

P23S, P24C, P4S, and P24S

P24T, P24CT, 487SX, 486SX, 486DX and 486DX2

Pins 1-2, 3-4

Pin 2-3

Not Installed

Real-Time Settings

| Jumper | Function | Setting |
| --- | --- | --- |
| W1 | Real-Time Clock Installed | IN |
| W5 |

To discharge Real-Time Clock

For normal operation (default)

IN

OUT

Monitor Selection

| Jumper | Function | Setting |
| --- | --- | --- |
| W2 |

Color

Mono

IN

OUT

Remaining “W”

| Jumper | Function | Setting |
| --- | --- | --- |
| W1 | Reserved | 1-2 |
| W7 |

Color Monitor

Mono Monitor

Short

Open

W16

AT Style Keyboard

PS/2 Style Keyboard

Open

| Short |
| --- |
| W17 | Reserved | 1-2 |
| W18 |

Clear RMA in RTC

| (may not be present) | Short |
| --- | --- |

Case and Peripheral Connections

| Jumper | Function | Setting |
| --- | --- | --- |
| J31 | Parallel Port Connector |
|  | J33 | Serial Port A |
|  | J34 | Serial Port B |
|  | J12 | Keyboard Connector |
|  | J6/J7 | Power Supply Connector |
|  | J32 | IDE Connector | Primary |
| J31 | Floppy Connector |
|  | J3 | External Battery | 1-battery positive; 2-N/C, 3-GND; 4-GND |
| J11 | Reset Switch | 1-GND; 2-GND |
| J5 | Turbo LED | 1-Signal; 2-GND |
| J4 | Turbo Switch | 1-Signal; 2-GND |
| J8 | Keylock/Power LED | 1-Power; 2-N/C; 3-GND; 4-5V DC |
| J10 | Speaker Connector |

1-Speaker; 2-N/C

| 3-GND; 4-5V DC |
| --- |
| J13 | External Keyboard |

1-Keyb lck, 2-data

3-N/C, 4-GND, 5-<+> 5V

Memory Configuration

| Bank 0 | Bank 1 | Bank 2 | Bank 3 | Total |
| --- | --- | --- | --- | --- |
| 4mb |
| 4mb |
| 4mb | 4mb |
|  | 8mb |
| 4mb | 4mb | 4mb |
| 12mb |
| 4mb | 4mb | 4mb | 4mb | 16mb |
| 16mb |
| 16mb |
| 4mb | 4mb | 16mb |
| 24mb |
| 16mb | 16mb |
|  | 32mb |
| 4mb | 16mb | 16mb |
| 36mb |
| 4mb | 4mb | 16mb | 16mb | 40mb |
| 16mb | 16mb | 16mb |
| 48mb |
| 16mb | 16mb | 16mb | 16mb | 64mb |