# TEST REPORT                               Dec . 27 . 1999

##### 5VIA73

ACORP  ELECTRONICS CORP.

8F, No.123-5 , Shing Teh RD. San Chung City , 
Taipei Hsien , Taiwan R.O.C.
Tel:886-2-2999-7188  Fax:886-2-2999-7177

http://www.acorp.com.tw

E-Mail:acorp@ms2.hinet.net

SPECIFICATION

01. Processor : Socket 7 Compatible Processor.

02. Chipset : VIA82C501/686 Chip set.

03. CPU Support : Intel , AMD , Cyrix and IDT.

04. Voltage Regulator : DIP SW ( 2.0V to 3.5V )

05. Bus CLK : 66/75/83/95/100/124 ... MHz.

06. Bus Architecture : 3 x 32 bit PCI Bus, 1 x 16 Bit ISA Bus.

07. L2 Cache Memory : On Board Pipeline SRAM 1 MB.

08. USB : Support 4 x Universal Serial Bas Port .

09. System Memory : 3 x 168 pin DIMM Socket 768M ( Max ).

10. On Board I/O : 1 x Floppy, 2 x Serial Ports, 1 x Parallel Port ( ECC,EPP,SPP ) ,

1 x Infrared Port ( IR ).

11. Power Support : ATX Power Connector Support.

12. BIOS : AWARD AGP BIOS with ACPI, Plug and Play Features 2MB Flash ROM,

Support CD-ROM , SCSI , LAN , LS120 boot.

13. Special Features : Temperature Senor ( Option ) , Warning by Sound , Auto Detec CPU

Thermal pin , Wake On Lan, wake on Modem, Wake on Alarm BUS,

Hard - ware Monitor ( option ).

14. DMA : Support Ultra DMA 33/66 .

15. Multimedia on Board : AC-97 Basic Audio.

16. VGA on Board : Trident 2x AGP VGA on Board.

17. Board Size : 22 x 23 cm ( AT Form ).

ACORP ELECTRONICS CORPORATON.                                                                                    Page  1
http://www.acorp.com.tw

PART A. SPECIFICATION TEST

System Specific

- System Specific Test

- System BIOS Test

- System Utility Test

- System Diagnostic & Certification Test

- Field (Stress) Test

PART B. OPERATING SYSTEM ENVIRONMENT TEST

- Microsoft Windows 95, 98 Operating System Test

- Microsoft Windows NT Operating System Test

- Operating System Field (Stress) Test

ACORP ELECTRONICS CORPORATON.                                                                                    Page  2
http://www.acorp.com.tw

PART A . SPECIFICATION TEST

2. System Specific Test

| CPU TEST |
| --- |
| Vender | Model | Voltage | Clock Multiplier | Bus Speed |
| Intel | AMD K6 – PR2 166 | 2.9V | 2.5 x | 66 MHz |
|  | AMD K6 – 233 | 3.2 V | 2.5 x | 66 MHz |
|  | AMD K6 II - 350 | 2.2 V | 3.5 x | 100 MHz |
|  | AMD K6 III – 450 | 2.4 V | 4.5 x | 100 MHz |
|  | Intel MMX – 166 | 2.8 V | 2.5 x | 66MHz |
|  | Intel MMX – 200 | 2.8 V | 3 x | 100 MHz |
| Memory Test |
| Type | Size | Vender | Component | Type | Amount | Status |
| 168 Pin DIMM module | 16 Mytes | NEC | D451682165-A10-7JF | PC66 | 3 | Pass |
|  | 32 Mytes | NEC | D4516821AG5-A10-7JF | PC66 | 3 | Pass |
|  |  | SIEMENS | HYB39S16800AT-8 | PC66 | 3 | Pass |
|  | 64 Mytes | Kti | JSV884T4A0A | PC100 | 3 | Pass |
|  |  | LGS | GM72V66S41CT75 | PC100 | 3 | Pass |
|  |  | SEC | KM48S8030CT-GH | PC100 | 3 | Pass |
|  |  | JMC | 8008KTW-SS | PC100 | 3 | Pass |
|  |  | ACORP | AP52836408313-7 | PC100 | 3 | Pass |
|  | 128 Mytes | HITACHI | HM5264805TTB60 | PC100 | 3 | Pass |
|  |  | MOSEL | V54C365864VCT75 | PC133 | 3 | Pass |
|  |  | NEC | D4564841G5-A80-9JF | PC100 | 3 | Pass |
|  |  | SEC (D) | KM48S8030CT-F10 | PC100 | 3 | Pass |
|  |  | SEC (S) | KM48S16030T-GL | PC100 | 3 | Pass |
|  |  | Kti | TSV884T4A0A | PC100 | 3 | Pass |
|  |  | Winbond | W986408BH-75 | PC133 | 3 | Pass |
|  | 256 Mytes | SEC | KM44S16030BT-GH | PC100 | 2 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  3
http://www.acorp.com.tw

| FDD Devices |
| --- |
| Type | Model | O.S. Environment | Status |
| 1.44 MB FDD | Mitsumi D353T6 | Win95 V950B Win NT V 4.0 | Pass |
|  | NEC FD1231H | Win98SE V4.10 | Pass |
|  | TEAC FD235FH | Win95 V950B | Pass |
|  | Panasonic JU-257A606P | MS-DOS V6.22 Win2000 2128 | Pass |
| 120MB FDD | Mitsubishi MF357G-111MA | Win95 V950B Win98SE V4.10 Windows NT 4.0 | Pass |
| Serial Port Devices |
| Type | Model | O. S. Environment | Status | Remark/Special setting |
| Mouse | Genius Serial Mouse | Win95 V 950B Win98SE V 4.10 Win NT V 4.0 | Pass |  |
|  | Logitech First Mouse | Win95 V 950B Win98SE V 4.10 | Pass |  |
|  | NEC King Mouse | Win95 V 950B Win98SE V 4.10 | Pass |  |
|  | DTK Mouse | Win95 V 950B MS-DOS V 6.22 Win2000 V2128 | Pass |  |
| PS2 Port Devices |
| Type | Model | O. S. Environment | Status | Remark/Special setting |
| Mouse | Microsoft PS/2 Mouse | Win NT V 4.0 Win98SE V 4.10 Win95 V950B | Pass |  |
|  | Logitech PS/2 Mouse | Win98SE V 4.10 Win2000 V2128 | Pass |  |
|  | AT&T PS/2 Mouse | Win95 V 950B Win98SE V 4.10 | Pass |  |
|  | DTK PS/2 Mouse | Win95 V 950B MS-DOS V 6.22 | Pass |  |
|  | Agiler PS/2 Mouse | Win98SE V4.10 Win95 V 950B MS-DOS V 6.22 | Pass |  |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  4
http://www.acorp.com.tw

| Parallel Port Devices |
| --- |
| Type | Model | O. S. Environment | Status | Remark/Special setting |
| Print | HP Laser Jet 5L | MS-DOS V 6.22 Win98SE V 4.10 Win2000 V2128 | Pass |  |
|  | EPSON Color 740 | Win95 V 950B Win98SE V 4.10 | Pass |  |
| USB Devices |
| Typer | Model | O. S. Environment | Status | Remark/Special setting |
| Mouse | USB Mouse | Win98SE V 4.10 | Pass |  |
| Keyboard | USB Keyboard | MS-DOS V 6.22 Win98SE V 4.10 | Pass |  |
| HUB | USB 4- Port HUB | Win98SE V 4.10 | Pass |  |
| Modem | USB Modem | Win98SE V4.10 Win95 V 950B | Pass |  |
| ZIP | IOEMGA Z100USB | Win98SE V 4.10 Win2000 2128 | Pass |  |
| Print | EPSON Color 740 | Win98SE V 4.10 | Pass |  |

2 . System BIOS Test

2.1 System CMOS Setup

| System BIOS Test |
| --- |
| Test Item | Status | Remark/Special setting |
| CMOS Setup Utility | Load BIOS Default | Pass |  |
|  | Load Setup Default | Pass |  |
|  | Supervisor Password | Pass |  |
|  | User Password | Pass |  |
|  | Save & Exit Setup | Pass |  |
|  | Exit Without Saving | Pass |  |
| Standard CMOS Setup Test | Sign-On Message And BIOS Information | Pass |  |
|  | POST error detection message Test | Pass |  |
|  | System Date and Time | Pass | Over 2000 year (BIOS /DOS/Win95/Win98) |
|  | Diskette A: / B: | Pass | None /1.44 MB |
|  | Hard Disk Drive | Pass | HDD Auto Detect/User type /None |
|  | Video System | Pass | EGA/VGA |
|  | System Memory | Pass |  |
|  | Extended Memory | Pass |  |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  5
http://www.acorp.com.tw

| System BIOS Test |
| --- |
| Test Item |  | Status | Remark/Special setting |
| BIOS Features Setup | Virus Warning | Pass | Enabled / Disabled |
|  | CPU Internal Cache | Pass | Enabled / Disabled |
|  | External Cache | Pass | Enabled / Disabled |
|  | Quick Power On Self Test | Pass | Enabled / Disabled |
|  | Boot Sequence | Pass | Floppy/LS,ZIP/SCSI HDD-0,1,2,3/CD-ROM LAN/Disabled |
|  | Swap Floppy Drive | Pass | Enabled / Disabled |
| Chipset Features Setup | On Chip USB | Pass | Enabled / Disabled |
|  | USB Keyboard Support | Pass | Enabled / Disabled |
|  | On Chip Sound | Pass | Enabled / Disabled |
| PNP/PCI Configuration | Resources controlled By | Pass | Auto/ Manual |
|  | Assign IRQ For USB | Pass | Enabled / Disabled |
| Integrated Peripherals | On Chip IDE Channe 0 | Pass | Enabled / Disabled |
|  | On Chip IDE Channe 1 | Pass | Enabled / Disabled |
|  | IDE Prefetch Mode | Pass | Enabled / Disabled |
|  | IDE HDD Block Mode | Pass | Enabled / Disabled |
|  | On –Chip Primary PCI IDE | Pass | Enabled / Disabled |
|  | On –Chip Secondary PCI IDE | Pass | Enabled / Disabled |
|  | Onboard FDC Controller | Pass | Enabled / Disabled |
|  | Onboard Serial port 1 | Pass | Auto/3F8/IRQ4/ Disabled |
|  | Onboard Serial port 2 | Pass | Auto/2F8/IRQ3/ Disabled |
|  | Onboard Parallel port | Pass | 3BC/IRQ7/ Disabled |
| Power Management Setup | ACPI Function | Pass | Enabled / Disabled |
|  | Power Management | Pass | User Define / Min Saving / Max Saving |
|  | Soft-off by PWR-BTTN | Pass | Delay 4 Sec / Instant-Off |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  6
http://www.acorp.com.tw

2.1 Boot sequence Test

| Boot Sequence Test |
| --- |
| Type | Peripheral device | O.S. Environment | Status | Features Tested |
| A , C | WD 28400 UDMA66 | MS-DOS V 6.22 Win98SE V 4.10 | Pass |  |
| C , A | IBM DTTA-351010 UDMA33 | MS –DOS V 6.22 Win98SE V 4.10 | Pass |  |
|  | Quantum 4300 SE UDMA 33 | Win95 V 950B NT WKS V 4.0 | Pass |  |
|  | Quantum CX6400AT UDMA 66 | Win98SE V 4.10 Win2000 V 2128 | Pass |  |
|  | Fujitsu MPC 3064AT UDMA 33 | NT WKS V 4.0 Win98SE V 4.10 | Pass |  |
|  | Maxtor 90845U3 DMA 66 | Win2000 V 2128 | Pass |  |
| A , CDROM , C | Fujitsu APC3064AT Teac CD-532E | NT WKS 4.0 | Pass |  |
|  | Quantum SE43A012 Pioneer Dr-A14S | WIN98SE V 4.10 | Pass |  |
| COROM ,C,A | Seagate 6531 SDR-520H | Win98SE V 4.10 | Pass |  |
|  | WD 28400 VUEGO 623A | WinNT V 4.0 Win98SE V 4.10 | Pass |  |
|  | Seagate ST38421A Creative Dxr2 | WinNT V 4.10 | Pass |  |
|  | Maxtor 82560A4 DCS 36x | WinNT V 4.10 Win98SE V 4.10 | Pass |  |
| C only | IBM DJNA-352500 UDMA 66 | MS-DOS V 6.22 WIN98SE V 4.10 | Pass |  |
| LS/ZIP , C | WD 36400 Mitsubushi MF357G -111MA | MS-DOS V 6.22 Win98SE V 4.10 | Pass |  |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  7
http://www.acorp.com.tw

3 System Utility Test

| System Utility |
| --- |
| Package Name | Version | Publisher | O.S. Environment | Status | Features Tested |
| CBROM Utility | 1.3 | Award | MS-DOS V 6.22 | Pass | Add NCR ROM |
| AFLASH Utility | 6.5 7.05 | Award | MS -DOS V 6.22 | Pass | Flash a new BIOS |
| MODBIN Utility | 4.50.75 | Award | MS -DOS V 6.22 Win95 V 950B | Pass | Utility BIOS Version |
| Bus Master Driver |
| Package Name | Primary IDE | Secondary IDE | O.S. Environment | Status |
|  | HDD (Mode/Speed) | CD-ROM (Mode/Speed) |  |  |
| Win98 Driver Ver : 4.16 | IBM DTTA-351010 UDMA 33 | PINNEER 36x | Win98SE V 4.10 | Pass |
|  | WD 36400 UDMA 33 | Teac CD-532E 32x | Win98 V 4.10 (Chinese ) | Pass |
|  | Fujitsu MPC3064AT UDMA 33 | Pioneer Dr-A14S 36x | Win98SE V 4.10 | Pass |
|  | Quantum CX6400AT UDMA 66 | Creative Dxr2 DVD 2x | Win98 V 4.10 | Pass |
|  | Maxtor 90845U3 UDMA 66 | VUEGO 632A 32x | Win98 V 4.10 | Pass |
| WinNT 4.0 Driver Ver : 4.16 | Fujitsu MPC3064AT UDMA 33 | Creative Dxr2 DVD 2x | Win NT V 4.0 | Pass |
|  | Quantum CX 64A013 DMA 66 | VUEGO 632A 32x | Win NT V 4.0 | Pass |
|  | IBM DCAA-34330 DMA 33 | Teac CD-532E 32x | Win NT V 4.0 | Pass |
|  | WD 28400 UDMA 66 | DCS C840P 40x | WinNT V4.0 | Pass |

4. System Utility Test

| System Utility |
| --- |
| Package Name | Version | Publisher | O.S. Environment | Status | Features Tested |
| Check It | V3.0 | Tochstone | MS-DOS V 6.22 | Pass |  |
| QAPLUS | V5.52 | Diagsoft | MS -DOS V 6.22 | Pass |  |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  8
http://www.acorp.com.tw

5. Fied (stress) Test

| Test Type |
| --- |
| Configuration | AMD K6 III-450 + 512 MB ( SDRAM 256 MB x 2 ) + On- Board IDE /AGP VGA/Sound + AHA-2940UW S9 + Intel 82558 LAN + |
| Test procedure | Win98SE & WinBench 99 demo Test . |
| Result | Pass | Duration | 72 Hours |

| Test Type |
| --- |
| Configuration | AMD K6 III - 450 + 384 MB ( SDRAM 128 MB x 3 ) + On- Board IDE /AGP VGA /Sound + IBM DJNA-352500 + 3Com 509B-TX LAN |
| Test procedure | Win98SE & WinStone 99 demo Test . |
| Result | Pass | Duration | 48 Hours |

| Test Type |
| --- |
| Configuration | AMD K6 II – 350 + 192MB ( SDRAM 64 MB x 3 ) + On- Board IDE /AGP VGA /Sound + Maxtor 90845U3 + RTL 8139B + RCVDL 56ACF Modem Card |
| Test procedure | Win98SE & Winstone 98 demo Test . |
| Result | Pass | Duration | 48 Hours |

| Test Type |
| --- |
| Configuration | AMD K6 - 233 + 192 MB (SDRAM 32 MB x 3 ) + On- Board IDE /AGP VGA / Sound + Quantum CX6400AT |
| Test procedure | Win98 & 3D MARK demo Test . |
| Result | Pass | Duration | 48 Hours |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  9
http://www.acorp.com.tw

PART B. OPERATING SYSTEM ENVIRONMENT TEST

1.Microsoft Windows Operating System Test

  - Software Compatibility Test

1.1.1 Operating System Compatility

| O.S Name | Version | Publisher | Status | Hardware configuration / Hard disk & Controller |
| --- | --- | --- | --- | --- |
| Windows 95 | V950B | Microsoft | Pass | On -Board IDE/AGP VGA/Sound + WD 28400 + PIONEER (36x) CD-ROM + Microsoft PS/2 Mouse |
| Windows 95 ( Chinese ) | V950B | Microsoft | Pass | On -Board IDE/AGP VGA/Sound + Quantum CX6400AT+ DCS C840P (40x) + Microsoft PS/2 Mouse |
| Windows 95 | V950B | Microsoft | Pass | AHA-2940UW + Quantum TM 3200 + TEAC CD-532E (32x) CD-ROM + logitech mouse |
| Windows 95 ( Chinese ) | V950B | Microsoft | Pass | Bus Logic SCSI + Quantum TM 3200 + VUEGO 632A (32X) CD-ROM + Microsoft PS/2 Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | On -Board IDE/VGA AGP/Sound + SDR-520H (DVD-ROM) + DTK PS/2 Mouse |
| Windows 98 (Chinese ) | 4.10 | Microsoft | Pass | On -Board IDE/AGP VGA + IBM DJNA-351010 + VUEGO 632A (32X) CD-ROM + NEC serial Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | AHA-2940UW + Quantum TM 3200 + SDR-520H (DVD-ROM ) + DTK PS/2 Mouse |
| Windows 98 (Chinese ) | 4.10 | Microsoft | Pass | BusLogic SCSI + Quantum TM 3200 + VUEGO 632A (32X) CD-ROM + NEC serial Mouse |
| Windows 98SE | 4.10 | Microsoft | Pass | On-Board IDE/AGP VGA/Sound + Maxtor ST90845U3 + Creative Dx2 (DVD ROM) + Microsoft PS/2 Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | On-Board IDE/AGP VGA/Sound + Quantum SE43A012 + PIONEER (36x) CD-ROM + AT&T PS/2 Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | On-Board IDE/AGP VGA/Sound + WD 36400 + Creative Dx2 (DVD ROM) + Microsoft PS/2 Mouse |
| Windows98 (Chinese ) | 4.10 | Microsoft | Pass | On-Board IDE/AGP VGA/Sound + Quantum CR8400AT + TEAC CD-532E (32x) CD-ROM + DTK PS/2 Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | On-Board IDE/AGP VGA/Sound + Seagate ST36531A + EPO (50x) CD-ROM + Microsoft PS/2 Mouse |
| Windows98SE | 4.10 | Microsoft | Pass | On-Board IDE/VGA AGP/Sound + WD 36400+ Pioneer (36X) CD-ROM + Microsoft PS/2 Mouse |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  10
http://www.acorp.com.tw

    - Application Software Compatibility

| Package Name | Version | Publisher | O. S. Environment | Status | Features tested |
| --- | --- | --- | --- | --- | --- |
| Office 95 | Professional | Microsoft | Win95 V950B Win98SE V 4.10 | Pass | Install From CD-ROM and execute Power point, Excel , Schedule Plus , Word Access application sample Files Open and Save Function . |
| Office 97 | Professional | Microsoft | Win95 V 950B Win98SE V 4.10 | Pass | Install From CD-ROM and execute Power point ,Excel , Schedule Plus , Word Access application sample Files Open and Save Function . |
| Windows 95 PLUS | V1.0 | Microsoft | Win95 V 950B | Pass | Install From CD-ROM and using Screen Saver Themes Change , mouse Pointer and Events Sound Change Function |
| Acrobat Reader | V 3.01 | Adobe | Win95 V 950B Win98SE V 4.10 | Pass | Install From CD-ROM Open PDF Files |
| PhotoShop | V4.0 | Adobe | Win95 V 950B Win98SE V 4.10 | Pass | Install From CD-ROM Open Sample and Edit JPG Files |
| PhotoShop | V5.0 | Adobe | Win95 V 950B Win98SE V 4.10 | Pass | Install From CD-ROM Open Sample and Edit JPG Files |
| PhotoImpact | V4.0 | Ulead | Win98 V4.10 ( Chinese ) | Pass | Install From CD-ROM Open Sample and Edit JPG Files |
| Frontpage 98 | V3.0.2 | Microsoft | Win98SE V4.10 | Pass | Install From CD-ROM Edit Html Files. |
| Winstone 98 | V 1.0 | Ziff -Davis | Win95 V 950B Win98SE V4.10 | Pass | Run Business Winstone98 |
| Winstone 99 | V 1.0 | Ziff -Davis | Win95 V 950B Win98SE V4.10 | Pass | Run Business Winstone99 |
| 3D Winbench 98 | V1.0 | Ziff -Davis | Win95 V 950B Win98SE V4.10 | Pass | All Test |
| 3D Winbench 99 | V1.0 | Ziff -Davis | Win95 V 950B Win98SE V4.10 | Pass | All Test |
| Winbench 99 | V1.0 | Ziff -Davis | Win95 V 950B Win98SE V4.10 | Pass | All Test |
| WinTach | V1.2 | Texas Instruments | Win95 V950B Win98SE V4.10 | Pass | Run Demo TEST |
| Speedy | V1.1 | Rights Reserved | Win95 V950B Win98SE V4.10 | Pass | Run Demo TEST |
| Fina Reality | V1.01 | VNU Euripean Labs | Win95 V950B Win98SE V4.10 | Pass | Run Demo TEST |
| 3DMARK | V1.0 | Futuremark | Win95 V950B Win98SE V4.10 | Pass | Run Demo TEST |
| CHECK IT 98 | V6.00.35 | TouchStone | Win98SE V4.10 | Pass | Run Function TEST |
| SCSI Card Controller |
| Card Type | Card Model | H .D .D | Secondary IDE | O.S. Environment | Status |
|  |  |  | CD-ROM (Mode/Speed) |  |  |
| SCSI ( PCI ) | AHA-2940UW | Quantum TM3200S | Teac CD-532E (32X) | Win95 V 950B Win98SE V 4.10 | Pass |
|  | Bus Logic | Quantum TM3200S | VUEGO 632A (32X) | Win95 V 950B (Chinese ) Win98SE V 4.10 | Pass |
|  | INIC-950OP | IBM DDRS-34560 | DCS C840P 40x | Win98SE V 4.10 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  11
http://www.acorp.com.tw

  - Hardware Compatibility Test

| IDE Controller |
| --- |
| Card type | Primary IDE | Secondary IDE | O.S. Environment | Status |
|  | HDD (Mode/Speed) | CD-ROM (Mode/Speed) |  |  |
| On-Board IDE ( PCI ) | WD 28400 UDMA 66 | VUEGO 632A (32X) | Win95 V 950B Win98SE V 4.10 | Pass |
|  | Fujitsu MPC3064AT UDMA 33 | Pioneer Dr-A14S (36X) | Win95 V 950B Win98SE V 4.10 Novell 3.12 | Pass |
|  | Maxtor 90845U3 UDMA 66 | SDR-520H (DVD 5X) | Win98SE V 4.10 Win2000 V 2128 | Pass |
|  | Seagate 6531 UDMA 33 | Teac CD-532E (32X) | Win95 V 950B (Chinese ) Win98SE V 4.10 | Pass |
|  | IBM DJNA-352500 UDMA 66 | Creative Dxr2 (DVD 2X) | Win95 V 950B Win98 V 4.10 (Chinese) | Pass |
|  | Seagate ST38421A UDMA 66 | Teac CD-532E (32X) | Win95 V 950B (Chinese ) Win98SE V 4.10 | Pass |
|  | Maxtor 90845U3 UDMA 66 | Creative Dxr2 (DVD 2X) | Win95 V 950B (Chinese-Simplified) Win98SE V 4.10 SCO UNIX | Pass |
|  | WD 36400 UDMA 33 | DCS C840P 40x | Win95 V 950B Win98SE V 4.10 Win2000 V 2128 | Pass |
|  | Quantum CR8400AT UDMA 66 | SDR-520H (DVD 5x) | Win95 V 950B Win98SE V 4.10 | Pass |
|  | Quantum SE43A012 UDMA 33 | Pionner Dr-A14S 36x | Win98 V 4.10 WinNT 5.0 B2 | Pass |
| Graphic Adapters |
| Card Type | Card Model | Peripheral Device | O.S. Environment | Status |
| VGA | S3 VIRGE /DX 4 MB | Quantum CR8400AT UDMA 66 | Win95 V 950B Win98 V 4.10 | Pass |
|  | S3 VIRGE /GX 4MB | WD 28400 UDMA 66 | Win95 V 950B Win NT V4.0 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  12

http://www.acorp.com.tw

| Ethernet adapters |
| --- |
| Card Type | Card Model | Peripheral Device | O.S. Environment | Status |
| Ethernet ( ISA ) | Acorp -908 | WD 28400 UDMA 66 | Win95 V 950B Win98SE V 4.10 Novell V 3.12 | Pass |
| Ethernet ( PCI ) | Acorp -970 | Quantum CX64A013 UDMA 66 | Win95 V 950B Win98SE V 4.10 WinNT V 4.0 | Pass |
|  | 3Com 3C905B -TX | IBM DTTA-351010 UDMA 33 | Win95 V 950B Win98SE V 4.10 | Pass |
|  | Intel 82558 | Maxtor 90845U3 UDMA 66 | Win98SE V 4.10 WinNT V 4.0 | Pass |
|  | RTL8139B/100MB | Seagate ST38421A UDMA 66 | Win98SE V 4.10 WinNT V 4.0 | Pass |
|  | RTL8029B/10MB | IBM DJNA-352500 UDMA 33 | Win98SE V 4.10 WinNT V 4.0 | Pass |
|  | 56 AMR CTR-21 | Quantum CR8400AT UDMA 66 | Win98SE V 4.10 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  13
http://www.acorp.com.tw

- Microsoft Windows NT 4.0 Server , workstation

Operating System Test

  - Software Compatibility Test

2.1.1 Operating System Compatility

| O.S Name | Version | Publisher | Status | Hardware configuration / Hard disk & Controller |
| --- | --- | --- | --- | --- |
| Windows NT Server | V 4.0 | Microsoft | Pass | On -Board IDE/AGP VGA/Sound + Seagate ST36421A + PIONEER (36x) CD-ROM + Microsoft PS/2 Mouse |
| Windows NT Server ( Chinese ) | V 4.0 | Microsoft | Pass | On -Board IDE/AGP VGA/Sound + IBM DTTA-351010 + DCS C840P (40x) CD-ROM + Genius Serial Mouse |
| Windows NT Workstation | V 4.0 | Microsoft | Pass | AHA-2940AW + Quantum TM 3200 + PIONEER (36x) CD-ROM + logitech mouse |
| Windows NT Workstaion ( Chinese ) | V 4.0 | Microsoft | Pass | BusLogic SCSI + Quantum TM 3200 + Teac CD-532E (32X) CD-ROM + Microsoft PS/2 Mouse |
| Windows NT Server | V 5.0 Beta2 | Microsoft | Pass | On –Board IDE/A¦GP VGA/Sound + SDR-520H (DVD-ROM ) + DTK PS/2 Mouse |
| Windows NT Workstation | V 5.0 Beta2 | Microsoft | Pass | On -Board IDE/AGP VGA/Sound + Quantum CR8400AT + VUEGO 623A (23X) CD-ROM + NEC serial Mouse |
| Windows 2000 | V 5.0 Beta3 | Microsoft | Pass | On-Board IDE/VGA AGP/Sound + WD 36400 + PIONEER (36X) CD-ROM + Microsoft PS/2 Mouse |

2.1.2 Application Software Compatibility

| Package Name | Version | Publisher | O. S. Environment | Status | Features tested |
| --- | --- | --- | --- | --- | --- |
| Winstone 98 | V 1.0 | Ziff -Davis | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From CD-ROM an Run business Winstone 98 High-End Winstone 98 Demo |
| Winstone 99 | V 1.0 | Ziff -Davis | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From CD-ROM an Run business Winstone 98 High-End Winstone 98 Demo |
| Microsoft Office 97 | Profession | Microsoft | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From CD-ROM and execute Powerpoint ,Excel , Schedule Plus , Word Access application sample Files Open and Save Function |
| WinTach | V 1.2 | Texas Inctruments | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From Floppy and Run TEST. |
| Final Reality | V 1.01 | VNU European Labs | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From Hard Disk and Run Demo TEST. |
| Speedy | V 1.1 | Rights Reserved | NT Server V 4.0 NT. WKS V 4.0 | Pass | Install From Hard Disk and Run TEST. |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  14
http://www.acorp.com.tw

    - Hardware Compatibility Test

| IDE Controller |
| --- |
| Card type | Primary IDE | Secondary IDE | O.S. Environment | Status |
|  | HDD (Mode/Speed) | CD-ROM (Mode/Speed) |  |  |
| On-Board IDE ( PCI ) | Seagate ST36531A UDMA 33 | Teac CD-532E (32X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Seagate ST36421A UDMA 33 | Pioneer Dr-A14S (36X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | IBM DTTA-351010 UDMA 33 | VUEGO 632A (32X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | WD 28400 UDMA 66 | SDR-520H (DVD 5X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | WD 36400 UDMA 33 | Creative Dxr2 (DVD 2X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Seagate ST36421A UDMA 33 | Teac CD-532E (32X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | IBM DTTA-351010 UDMA 33 | DCS C840P 40x | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | WD 36400 (DMA 33) | VUEGO 632A (32X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | WD 28400 UDMA 66 | SDR-520H (DVD 5X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Quantum SE43A012 UDMA 33 | Pioneer Dr-A14S (36X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Maxtor 90845U3 UDMA 66 | Creative Dxr2 (DVD 2X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
| IDE Controller |
| Card type | Primary IDE | Secondary IDE | O.S. Environment | Status |
|  | HDD (Mode/Speed) | HDD (Mode/Speed) |  |  |
| On-Board IDE ( PCI ) | Quantum CX6400AT UDMA 66 | Quantum CR8400AT UDMA 66 | DOS V 6.22 Win95 V 950 B | Pass |
|  | Fujitsu MPC3064AT UDMA 33 | Quantum SE43A012 UDMA 33 | Win95 V 950 B Win98 V 4.10 | Pass |
|  | IBM DTTA- 351010 UDMA 33 | WD 28400 UDMA 66 | Win98 V 4.10 OS2 WARP 4 | Pass |
|  | WD 28400 UDMA 66 | IBM DTTA-351010 UDMA 33 | DOS V 6.22 WinNT V 4.0 | Pass |
|  | Fujitsu MPC3043AT UDMA 33 | WD 36400 UDMA 33 | Win98 V 4.10 WinNT V 4.0 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  15
http://www.acorp.com.tw

| SCSI Card Controller |
| --- |
| Card Type | Card Model | H .D .D | Secondary IDE | O.S. Environment | Status |
|  |  |  | CD-ROM (Mode/Speed) |  |  |
| SCSI ( PCI ) | AHA-2940UW | Quantum TM3200S | Teac CD-532E (32X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Bus Logic | Quantum TM3200S | DCS C840P 40x | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | INIC-950OP | Quantum PXO4L011-4.5L | Pioneer Dr-A14S (36X) | NT Server V 4.0 NT. WKS V 4.0 | Pass |

| Ethernet adapters |
| --- |
| Card Type | Card Model | Peripheral Device | O.S. Environment | Status |
| Ethernet ( ISA ) | Acorp -908 | WD 28400 UDMA 66 | NT Server V 4.0 NT. WKS V 4.0 | Pass |
| Ethernet ( PCI ) | Intel 558 LAN | WD 36400 UDMA 33 | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | Acorp -970 | Seagate ST36421A DMA 33 | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | 3Com 905B-TX | IBN DTMST-351010 UDMA 66 | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | RTL8139B/100 MB | Quantum CX64A013 UDMA 66 | NT Server V 4.0 NT. WKS V 4.0 | Pass |
|  | RTL8029B/10 MB | Quantum CX64A013 UDMA 66 | NT Server V 4.0 NT. WKS V 4.0 | Pass |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  16
http://www.acorp.com.tw

3. Operating System Fied (stress) Test

| Test Type Windows NT 4.0 Server Operating System |
| --- |
| Configuration | AMD K6 III - 450+ 512 MB ( SDRAM 256 MB x 2 ) + On- Board IDE /AGP VGA /Sound + Quantum CR8400AT + Intel 82558 LAN |
| Test procedure | High-End Winstone 99 demo Test . |
| Result | Pass | Duration | 48 Hours |

| Test Type Windows 98 Operating System |
| --- |
| Configuration | AMD K6 III – 450 + 384 MB (SDRAM 128 MB x 3 ) + On- Board IDE /AGP VGA /Sound + IBM DTTA-351010 + RTL 8139B LAN |
| Test procedure | Business Winstone 99 demo Test . |
| Result | Pass | Duration | 48 Hours |

| Test Type Windows NT 4.0 workstation Operating System |
| --- |
| Configuration | AMD K6 II - 350 + 256 MB (SDRAM 128 MB x 2 ) + On- Board IDE/AGP VGA /Sound + Quantum + 3Com 905B-TX |
| Test procedure | High-End WinBench 99 demo Test . |
| Result | Pass | Duration | 72 Hours |

| Test Type Windows 95 Operating System |
| --- |
| Configuration | AMD K6 – 233 + 192 MB (SDRAM 64 MB x 3 ) + On- Board IDE/AGP VGA /Sound + Seagate ST38421A + RTL 8029B LAN |
| Test procedure | Business Wintone 98 demo Test . |
| Result | Pass | Duration | 48 Hours |

ACORP ELECTRONICS CORPORATON.                                                                                    Page  17
http : // www.acorp.com.tw

Manager :                  Supervisor :

Tester :

ACORP ELECTRONICS CORPORATON.                                                                                    Page  18
http://www.acorp.com.tw