Jumper Table Summary of MX58 Plus
Setting the CPU Voltage

Jumper Settings CPU Type Vcore S4 S5 S6 S7 S8 INTEL P54C Single Voltage 3.45V OFF ON ON ON OFF INTEL P55C Dual Voltage 2.8V OFF OFF OFF ON OFF AMD K5 Single Voltage 3.52V ON ON ON ON OFF AMD K6-166/200 Dual Voltage 2.9V ON OFF OFF ON OFF AMD K6-233 Dual Voltage 3.2V OFF OFF ON ON OFF AMD K6-266/300 Dual Voltage 2.2V OFF ON OFF OFF OFF AMD K6-II Dual Voltage 2.2V OFF ON OFF OFF OFF Cyrix 6x86 Single Voltage 3.52V ON ON ON ON OFF Cyrix 6x86L Dual Voltage 2.8V OFF OFF OFF ON OFF Cyrix M2 Dual Voltage 2.9V ON OFF OFF ON OFF IDT C6 Single Voltage 3.52V 3.3V ON ON ON OFF ON ON ON ON OFF OFF Warning: Make sure that you have installed CPU fan properly if Intel PP/MT-233 or AMD K6 is being selected to use. It may cause your system unstable if you can not meet the heat dissipation requirement from above CPU. It is recommended to adopt larger fan on these CPU for better air flow in the system. Tip: Normally, for single voltage CPU, Vcpuio (CPU I/O Voltage) is equal to Vcore, but for CPU that needs dual voltage such as PP/MT (P55C) or Cyrix 6x86L, Vcpuio is different from Vcore and must be set to Vio (PBSRAM and Chipset Voltage). The single or dual voltage CPU is automatically detected by hardware circuit.

Selecting the CPU Frequency S1 S2 S3 CPU FrequencyRatio OFF ON ON OFF ON ON OFF OFF OFF OFF ON ON OFF ON ON OFF OFF OFF OFF OFF ON ON ON ON 1.5x (3.5x) 2x (6x) 2.5x (1.75x) 3x 4x 4.5x 5x 5.5x JP4 JP5 JP6 CPU External Clock 2-3 2-3 1-2 2-3 1-2 2-3 2-3 2-3 2-3 1-2 2-3 1-2 1-2 2-3 1-2 1-2 2-3 2-3 50MHz 55MHz 60MHz 66MHz 75MHz 83MHz Warning: SIS 5598 chipset supports maximum 75 MHz external CPU bus clock, the 83MHz settings are for internal test only, set to 83MHz exceeds the specification of the chipset, which may cause serious system damage. INTEL Pentium CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 P54C 75 75MHz = 1.5x 50MHz OFF OFF OFF 2-3 & 2-3 & 1-2 P54C 90 90MHz = 1.5x 60MHz OFF OFF OFF 1-2 & 2-3 & 1-2 P54C 100 100MHz = 1.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 P54C 120 120MHz = 2x 60MHz ON OFF OFF 1-2 & 2-3 & 1-2 P54C 133 133MHz = 2x 66MHz ON OFF OFF 2-3 & 1-2 & 1-2 P54C 150 150MHz = 2.5x 60MHz ON ON OFF 1-2 & 2-3 & 1-2 P54C 166 166MHz = 2.5x 66MHz ON ON OFF 2-3 & 1-2 & 1-2 P54C 200 200MHz = 3x 66MHz OFF ON OFF 2-3 & 1-2 & 1-2 INTEL Pentium MMX CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 PP/MT 150 150MHz = 2.5x 60MHz ON ON OFF 1-2 & 2-3 & 1-2 PP/MT 166 166MHz = 2.5x 66MHz ON ON OFF 2-3 & 1-2 & 1-2 PP/MT 200 200MHz = 3x 66MHz OFF ON OFF 2-3 & 1-2 & 1-2 PP/MT 233 233MHz = 3.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 Cyrix 6x86 & 6x86L CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 P120+ 100MHz = 2x 50MHz ON OFF OFF 2-3 & 2-3 & 1-2 P133+ 110MHz = 2x 55MHz ON OFF OFF 2-3 & 2-3 & 2-3 P150+ 120MHz = 2x 60MHz ON OFF OFF 1-2 & 2-3 & 1-2 P166+ 133MHz = 2x 66MHz ON OFF OFF 2-3 & 1-2 & 1-2 P200+ 150MHz = 2x 75MHz ON OFF OFF 1-2 & 2-3 & 2-3 Cyrix M2 CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 MX-PR166 150MHz = 2.5x 60MHz ON ON OFF 1-2 & 2-3 & 1-2 MX-PR200 166MHz = 150MHz= 2.5x 2x 66MHz 75MHz ON ON ON OFF OFF OFF 2-3 & 1-2 & 1-2 1-2 & 2-3 & 2-3 MX-PR233 200MHz = 166MHz= 3x 2x 66MHz 83MHz OFF ON ON OFF OFF OFF 2-3 & 1-2 & 1-2 2-3 & 1-2 & 2-3 MX-PR266 233MHz = 3.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 MX-PR300 225MHz= 233MHz= 240MHz 3x 3.5x 4x 75MHz 66MHz 60MHz OFF OFF ON ON OFF OFF OFF OFF ON 1-2 & 2-3 & 2-3 2-3 & 1-2 & 1-2 1-2 & 2-3 & 1-2 AMD K5 CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 PR75 75MHz= 1.5x 50MHz OFF OFF OFF 2-3 & 2-3 & 1-2 PR90 90MHz = 1.5x 60MHz OFF OFF OFF 1-2 & 2-3 & 1-2 PR100 100MHz = 1.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 PR120 90MHz = 1.5x 60MHz OFF OFF OFF 1-2 & 2-3 & 1-2 PR133 100MHz = 1.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 PR166 116MHz = 1.75x 66MHz ON ON OFF 2-3 & 1-2 & 1-2 AMD K6 CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 K6-166 166MHz = 2.5x 66MHz ON ON OFF 2-3 & 1-2 & 1-2 K6-200 200MHz = 3x 66MHz OFF ON OFF 2-3 & 1-2 & 1-2 K6-233 233MHz = 3.5x 66MHz OFF OFF OFF 2-3 & 1-2 & 1-2 K6-266 266MHz= 4x 66MHz ON OFF ON 2-3 & 1-2 & 1-2 K6-300 300MHz= 4.5x 66MHz ON ON ON 2-3 & 1-2 & 1-2 K6-2 300 300MHz= 4.5x 66MHz ON ON ON 2-3 & 1-2 & 1-2 K6-2 333 333MHz= 5x 66MHz OFF ON ON 2-3 & 1-2 & 1-2 K6-2 366 366MHz= 5.5x 66MHz OFF OFF ON 2-3 & 1-2 & 1-2 K6-2 400 400MHz= 6x 66MHz ON OFF OFF 2-3 & 1-2 & 1-2 IDT C6 CPU Core Frequency Ratio External Bus Clock S1 S2 S3 JP4 & JP5 & JP6 C6-150 150MHz = 2x 75MHz ON OFF OFF 1-2 & 2-3 & 2-3 C6-180 180MHz = 3x 60MHz OFF ON OFF 1-2 & 2-3 & 1-2 C6-200 200MHz = 3x 66MHz OFF ON OFF 2-3 & 1-2 & 1-2 Note: Cyrix 6x86, 6x86MX (M2) and AMD K5 CPU use P-rating for the reference of CPU benchmark compared with INTEL P54C, their internal core frequency is not exactly equal to P-rating marked on the CPU. For example, Cyrix P166+ is 133MHz but performance is almost equal to P54C 166MHz and AMD PR133 is 100MHz but performance is almost equal to INTEL P54C 133MHz.

Clear CMOS JP14 Clear CMOS 1-2 2-3 Normal operation (default) Clear CMOS

Setting PCI Clock JP8 Setting PCI Clock 1-2 2-3 Sync (default) Async

Disable Onboard VGA JP11 Disable Onboard VGA 1-2 2-3 Enabled (default) Disabled

Disable Onboard Audio JS1 Disable Onboard Audio 1-2 2-3 Enabled (default) Disabled